## Slide 1: University at Buffalo SAE Clean Snowmobile Team
Presented By
Noor Jariri
Nick Lanzano
Team Members
Matt Egan Pete Casey
Nate Sutorious Anthony Marcheillo
Pat O’Byrne Dave Stedman

## Slide 2: Design Considerations
Environment
Decreased Emissions
Quieter Operation
Lowered Fuel Consumption
Manufacturer
Low Cost/High Product Quality
System Simplicity
Durability
Operator
Adequate Performance
Improved Handling
Enhanced Fuel Economy

## Slide 3: Engine Selection
Low HC, CO, and NOx emissions
High torque output
Low BSFC
Engine longevity and reliability
Low WOT exhaust noise
Briggs and Stratton DM-954DT
3 Cylinder Liquid Cooled Diesel
Indirect Fuel Injection System
Bosch VE Injection Pump
260 g/kW-hr BSFC

## Slide 4: Intercooler System
Design and Implementation
Decrease IAT’s for lowered NOx emissions
Efficient Bell Intercoolers core
Low intake tract volume
Effective packaging
Testing and Validation

## Slide 5: Turbocharger System
Design and Implementation
Garrett GT1541-V
Increase compressor efficiency and turbine flow capability
Improve exhaust flow
Correct turbocharger orientation and packaging
Factory Exhaust Manifold
Designed Exhaust Manifold

## Slide 6: Turbocharger System
Testing and Validation

## Slide 7: Cooling System
Design and Implementation
CPC ¾” Quick Disconnects impeded coolant flow
Mishimoto Aluminum Radiator
Quick Disconnects placed in parallel for easy system bleeding
Testing and Validation
Steady State Coolant Temperatures (*F) |  | 
Engine Load | With CPC Quick Disconnects | Without CPC Quick Disconnects
0% | 180 | 168
20% | 181 | 172
40% | 185 | 176
60% | 193 | 180
80% | 210 | 180
100% | 225 | 180

## Slide 8: Eco-System
Design and Implementation
User selectable performance or economy mode
Arduino Microcontroller varies boost and fuel based upon mode, EGT and MAP

## Slide 9: Eco-System
Testing and Validation
5-Mode Testing of Eco-System
Factory 32 hp increased to 48 hp in Eco-mode and 55 hp in Power-mode
Eco Mode attained E-score of 208

## Slide 10: Suspension System
Design and Implementation
Team Fast M10 Rear Suspension System
Fox Float II Front Shocks
C&A Pro Skis
Improved handling by lateral load transfer decrease
Testing and Validation
Shock Pressure tuning by slalom and circle testing

## Slide 11: Sled Overview
Extremely low HC, CO and NOx emissions
High fuel economy
Adequate power output for a snowmobile
Quiet operation
Durable and simple design

## Slide 12: Sponsors

## Slide 13: Questions? Thank you for your time!