## Slide 1: University at Buffalo SAE Clean Snowmobile Team
Presented By
Anthony Marchesiello
Nick Lanzano
Team Members
Nicholas Marchesiello Ryan Ball
Andrew Kruger Steven Widdis
Zachery Willis Alex Demay
Jeff D’Angelo

## Slide 2: Design Considerations
Environment
Decreased Emissions
Quieter Operation
Lowered Fuel Consumption
Manufacturer
Low Cost/High Product Quality
System Simplicity
Increased Durability
Operator
Extended Operation Period
Increased Towing Capacity
Extended Fuel Range

## Slide 3: Engine Selection
Low HC, CO, and NOx emissions
High Torque Output
Low BSFC
Engine Longevity and Reliability
Low WOT Exhaust Noise
Briggs and Stratton DM-954DT
3 Cylinder Liquid Cooled Diesel
Indirect Fuel Injection System
Bosch VE Injection Pump
260 g/kW-hr BSFC

## Slide 4: Turbocharger System
Design and Implementation
Garrett GT1541-V
Increased Compressor Efficiency and Turbine Flow Capability
Improved Exhaust Flow
Correct Turbocharger Orientation and Packaging

## Slide 5: Turbocharger System
Testing and Validation

## Slide 6: Belt Drive
Design Validation
Design and Implementation
Custom 6061 Aluminum Back Plate and Bracket
Increased Drivetrain Efficiency
Ease of Maintenance
Correct Final Drive Ratio
Final Drive Calculations |  | 
Drive System | Chain (stock) | 2015 Belt Drive
Drive Teeth | 22 | 32
Driven Teeth | 43 | 53
Drive Ratio | 1.95 | 1.66
Top Speed | 48.7 | 60.7

## Slide 7: Cooling System
Design and Implementation
Stock Track Heat Exchangers
Removed Flow Restrictions by Streamlining Fluid Flow
Testing and Validation
Steady State Coolant Temperatures (*F) |  |  | 
Engine Load | CPC Quick Disconnects | No CPC Quick Disconnects | No CPC Quick Disconnects, Heat Exchangers
0% | 180 | 168 | 175
20% | 181 | 172 | 173
40% | 185 | 176 | 172
60% | 193 | 180 | 170
80% | 210 | 180 | 168
100% | 225 | 180 | 164

## Slide 8: Suspension System
Design and Implementation
Team Fast M10 Rear Suspension System
Fox Float II Front Shocks
C&A Pro TRX Skis
Improved Towing Capacity Through Increased Traction
Testing and Validation
100 ft. Acceleration Test
Track Lug Height Comparison |  | 
Lug Height (Inch) | Unloaded Times (sec) | Loaded Times (sec)
1.063 | 7.017 | 10.606
1.5 | 6.076 | 8.007

## Slide 9: Sled Overview
Extremely low HC, CO and NOx Emissions
High Fuel Economy
Adequate Power Output for a Utility Snowmobile
Quiet Operation
Durable and Simple Design

## Slide 10: Sponsors

## Slide 11: Questions? Thank you for your time!