## Slide 1: University at Buffalo SAE Clean Snowmobile Team
Presented By
Anthony Marchesiello
Nick Marchesiello
Andrew Kruger Jeff D’Angelo Casey Amidon

## Slide 2: Design Considerations
Environment
Decreased Emissions
Quieter Operation
Lowered Fuel Consumption
Manufacturer
Low Cost/High Product Quality
System Simplicity
Increased Durability
Operator
Extended Operation Period
Increased Towing Capacity
Extended Fuel Range

## Slide 3: Engine Selection
Low HC, CO, and NOx emissions
High Torque Output
Low BSFC
Engine Longevity and Reliability
Low WOT Exhaust Noise
Mercedes-Benz/Smart OM 660
3 Cylinder Liquid Cooled Diesel
Direct Fuel Injection System
216 g/kW-hr BSFC

## Slide 4: Engine Output
Horsepower | 54.5 @ 3942 rpm
Torque | 84.7 @ 2460 rpm

## Slide 5: Engine Adaptation
6061 Aluminum Alloy
175 lb compressive force
FoS of 9.88

## Slide 6: Emissions System
Design and Implementation
Emitec Diesel Particulate Filter (DPF) - Passive System
Emitec Diesel Oxidation Catalyst (DOC)
DOC optimized for NO2 production, reducing HCs and CO
Both filters require higher EGTs
DPF
DOC
Exhaust Flow Direction
77% Reduction in particulate
90% reduction in HCs and CO

## Slide 8: Emissions System
Testing and Validation

## Slide 9: Suspension System
Design and Implementation
Fox Float II Front Shocks
Curve Industries XS Skis
Stud Boy 9” Shaper bars
Improved Towing Capacity Through Increased Traction

## Slide 10: Sled Overview
Extremely low HC, CO and NOx Emissions
High Fuel Economy
Adequate Power Output for a Utility Snowmobile
Quiet Operation
Durable and Simple Design

## Slide 11: Sponsors

## Slide 12: Questions? Thank you for your time!

## Slide 13: Suspension System
Design and Implementation
Team Fast M10 Rear Suspension System
Fox Float II Front Shocks
C&A Pro Skis
Improved handling by load transfer decrease
Testing and Validation
Shock Pressure tuning by slalom and circle testing

## Slide 14: Suspension System
100 ft. Straight Acceleration Data |  |  |  | 
Lug Height | 1" | 1" tow | 1.5" | 1.5" tow
Trial 1 (sec) | 7.23 | 10.66 | 5.94 | 8.34
2 | 6.77 | 10.3 | 5.8 | 7.56
3 | 7.13 | 11.2 | 6.69 | 7.92
4 | 7.02 | 10.85 | 6.12 | 8.23
5 | 6.88 | 9.96 | 5.84 | 7.89
6 | 6.8 | 10.54 | 6.03 | 7.95
7 | 7.2 | 11.12 | 6.37 | 8.17
8 | 7.12 | 10.79 | 5.97 | 8.04
9 | 7.08 | 10.23 | 6.21 | 8.01
Trial 10 (sec) | 6.94 | 10.41 | 5.79 | 7.96
Avg. (sec) | 7.017 | 10.606 | 6.076 | 8.007