## Slide 1: University at Buffalo SAE Clean Snowmobile Team
Presented By
Austin Keppler
Ethan Schonhaut

## Slide 2: Design Considerations
Environment
Decreased Emissions
Quieter Operation
Lowered Fuel Consumption
Manufacturer
Low Cost/High Product Quality
System Simplicity
Increased Durability
Operator
Extended Operation Period
Increased Towing Capacity
Extended Fuel Range

## Slide 3: Engine/Chassis Selection
Bearcat 3000 Lt/Kymco 700cc 4-Stroke
Small Displacement/Low Emission/High power
Low BSFC
Engine Longevity and Reliability
Low WOT Exhaust Noise
Low Cost
Kymco 700 4-Stroke
2 cylinder
Fuel Injection System

## Slide 4: Engine Output
Arctic Cat AVL Dyno Emissions 2017
Power: 47 hp
Torque: 74 ft*lbs

## Slide 5: Engine Control
Replaced a piggy back system with MoTeC M130 ECU
Complete control over engine parameters

## Slide 6: Sensors
Bosch LSU4.9 wideband O2 sensor
GM flex fuel sensor
Upgraded to a 2 bar MAP sensor

## Slide 7: Tuning
Tuned to be sure engine was running close to stoichiometric (14.8 - 15.1) during operating conditions
  Bosch LSU4.9 Wideband O2 sensor and gauge
Tuned to add more fuel during cold start and idle (12.5 - 13.2)

## Slide 8: Turbo System
Design and Implementation
BorgWarner KP35
Precision Turbo 38mm external wastegate
Custom log manifold to fit space constraints
Cold air intercooler intake with heat exchanger
TurboSmart blow off valve

## Slide 9: Exhaust System
Modular exhaust system
Flowmaster catalytic converter
Dynomax Performance muffler

## Slide 10: Suspension, Track, and Steering
Design and Implementation
Curve Industries XS Skis
Woody’s studs for increased traction
Improved handling over stock utility skis and track

## Slide 11: Sled Overview
Low HC, CO emissions
Quiet operation
Durable and simple design (cheap to manufacture)

## Slide 13: Questions? Thank you for your time!