## Slide 1: University at Buffalo SI
Austin Keppler / Austin Ocwieja

## Slide 2: Last Years Results
Bearcat 3000 Chassis
700 Ctec4 2 cylinder four stroke engine
Exhaust manifold failure during endurance event

## Slide 3: 2019 Clean Snowmobile Strategy
Build a snowmobile that can be built upon in future years
Sustain performance characteristics that would make the snowmobile marketable
Focus on reducing noise output of both the engine and chassis

## Slide 4: Chassis
2017 ZR 3000
  Lightweight
  Trail suited
  Same basic platform as previous year

## Slide 5: Engine
Arctic Cat Ctec4
  700cc 2 Cylinder Four Stroke

## Slide 6: Engine Management
Motec M130
Closed Loop Fuel Tuning
Flex Fuel Compatable
Tuned to run at stoichiometric combustion

## Slide 7: Turbocharger
BorgWarner KP 35
Utilize these parameters to locate efficiency on compressor map

## Slide 8: Exhaust
Factory Exhaust Manifold
Precision Turbo Wastegate
Honda Muffler
3 Way Magnaflow Catalytic Converter
Custom Built Resonator

## Slide 9: Resonator
Identified droning frequency around ~59 - 60 Hz

## Slide 10: Resonator

## Slide 11: Chassis Noise Reduction
Tested several different materials
Foam
Lizard Skin
Spray Paint
Enclosed test fixture

## Slide 12: Test Results
Chart: Frequency (Hz)
| 100 | 200 | 300 | 400 | 500 | 600 | 700
Black Foam | 97.8 | 96.4 | 91.6 | 90.5 | 104.6 | 92.5 | 97.9
Grey Foam | 94.3 | 94.1 | 84.8 | 98.3 | 104.2 | 91.3 | 98.5
Lizard | 99.7 | 98.9 | 93.9 | 97.6 | 98.5 | 95.8 | 98.6
Paint | 99.4 | 100.5 | 100.4 | 98.1 | 99.3 | 98.6 | 100.5
Bare Metal | 99.8 | 100.1 | 100.9 | 100.1 | 99.7 | 100.3 | 101.3

## Slide 13: Conclusion
Successfully created a low noise emitting snowmobile
Unfortunately ran into small undetected problems that led to the failure of the snowmobile

## Slide 14: Thank You
Austin Keppler – Mechanical Engineering / MBA
alkepple@buffalo.edu
Austin Ocwieja – Mechanical Engineering / MBA
austinoc@buffalo.edu