## Slide 1: Clarkson Winter Knights
Austin Donhauser
Brad
Cyr

## Slide 2
Design Intent
Reliability
Cost Effectiveness
Exceptional Fuel Economy
Reduced Emissions
Cold Start Ability
Low Weight

## Slide 3
2018 Polaris Switchback SP
144” Long Track
Large Engine Bay
Low Weight
Superior Suspension and Handling

## Slide 4
Diesel Engine Selection
Selection Matrix
  Weights based on level of importance
  Most Important: Availability, Size, HP
Perkins 403D-07 – Best Choice
  Meets US EPA Tier 4 Emissions Standards
  Specs
    20.5 HP
    32.8 lb-ft @ 2200 RPM
    156.5 lbs Dry Weight
    Relatively Small Diesel Engine Size

## Slide 5
Governor Spring
Generator Model Engine (403D-07G)
  Rated 1800 RPM, 10.5 HP
  Engine Speed too low for application
Engine Speed Controlled by Governor
  Stiffer Governor Spring Increased RPM’s
Caterpillar C0.7 3600RPM Model Spring Installed

## Slide 6
Performance Increases
Chart: Power vs Engine Speed Perkins 403D-07
| 2400 | 2000 | 1700
403D-07 as Advertised | 19.4 | 16.1 | 12.1
403D-07 as Received | 13.6 | 12.2
New Governor Spring | 15 | 20.3 | 26.9 | 27.3 | 26.2 | 25.5 | 23.7 | 21.3 | 18.6 | 15.8 | 14.8 | 11.6 | 10.6 | 9.5 | 8.6
Chart: Torque vs Engine Speed Perkins 403D-07
| 1998 | 1883
403D-07 as Received | 35.6 | 34
New Governor Spring | 22 | 29 | 41.4 | 43.8 | 45.4 | 45.5 | 44.5 | 44.3 | 41.8 | 40 | 38.6 | 35.8 | 34.1 | 33 | 30.1
403D-07 as Advertised | 63 | 61.8 | 58.3

## Slide 7
Dry Sump Oil System
Engine bay height constraints
  Cut oil pan 2”
  Reduction in oil capacity beyond safe limits
Stock Capacity: 0.75 Gal
Dry Sump Capacity: 0.86 Gal
Scavenge Pump
  CXRacing 3.7GPM
Used in many race applications,
allows for steady oil supply at
all times

## Slide 8
Turbocharger Selection
Garrett by Honeywell SAE Program
GT-12Z best fit for
application
  65% Efficiency @ 35HP

## Slide 9
Turbocharger and Intercooler
  Bell Intercooler w/ cooling fan
    Efficiently cools compressed air from turbo
  Turbocharger
    Increase power output
    Reduce emissions by leaning fuel/air mixture
    Increase fuel economy

## Slide 10
Diesel Oxidation Catalyst
Faurecia DOC (Diesel Oxidation Catalyst)
Oxidizes CO, HC, and small fractions of PM
High temperature increases efficiency
Placed as close as possible to manifold for highest temperatures

## Slide 11
Diesel Particulate Filter
Faurecia PDPF (Partial Diesel Particulate Filter)
Downstream of DOC
Made from SiC or TiAl
Filtration is >99% efficient after soot coverage

## Slide 12
Cold Start Reliability
Stock Battery replaced with Shorai LFX Lithium Ion Battery
  550 CCA allows for fast cold starts
Denso glow plugs
  Increase pre-combustion chamber temperature to aid in cold start ignition

## Slide 13
Future Plans
Future plans of SCR incorporation and Diesel Injection
Mechanical Fuel Injection  Electronic Common Rail Fuel Injection
Clutch calibration for higher speed

## Slide 14: Thank you
Questions?