## Slide 1: Clarkson Winter Knights
Austin Donhauser
Scott Deichmann

## Slide 2
Design Intent
Reliability
Cost Effectiveness
Practicality
Increased Fuel Economy
Reduced Emissions
E00-E85

## Slide 3: 2017 Ski-doo Renegade Sport
Best Available Technology (BAT)
600 ACE has proven successful
Best in class fuel economy
Familiar chassis

## Slide 4: Engine Management
Motec M130
  Exceptional customer support
  Many inputs/outputs to support sled modifications
  User friendly software – M1 Tune/Build
  EGR control
  Active Exhaust Valve Control
Motec LTCD Dual Lambda Controller
  Individual cylinder fuel/timing trim
  Bosch 4.9 LSU Oxygen Sensors

## Slide 5: Ethanol Compatibility
GM Continental Flex Fuel Sensor
  Frequency 50-150Hz Signal Output
Zeitronix ECA (Ethanol Composition Analyzer)
  Output of 0-5V analog signal
M130 reads via analog input
  Tables: 0% ethanol, 85% ethanol
  Creates scaling table for values in between

## Slide 6: Engine Calibration
Land & Sea DYNOmite Dynamometer Water Brake
  Changing loads and RPM to create engine efficiency table

## Slide 7: Exhaust
Emitec-Continental 3-Way catalyst
  Designed specifically for ethanol based fuels
Custom 2 to 1 header pipe
Fiberglass packed muffler
  Used inside stock shell to maintain stock fit
Exhaust output aimed at track
DEI Engineering Titanium Heat Wrap

## Slide 8: Active Exhaust Valve
2” Exhaust Cutout
Electronically controlled by M130
  Based on throttle position
    0% Throttle – 5% opened valve
    Exponential curve to open valve for unaffected performance
Sound testing procedures
  Idle (1800 rpm)
  2 ft from open side panel, 2 ft from ground
  Decrease of 5db on average using Larson Davis sound testing equipment

## Slide 9: EGR (Exhaust Gas Recirculation)
Wells 4355 EGR valve
  90º Angle for fitment
ECU Programming
  Activate based on engine load
  Removes fuel from tables for leaner mixture
EGR Testing
  Testing using DYNOmite and Snap-On Gas Analyzer
  Engine Speed maintained at 2500 rpm

## Slide 10: Driveshaft & Rear Suspension
R-Motion Rear Suspension
Camso Ice Attak 137” Track
Ski-Doo SilentDrive
Hiperfax Slides

## Slide 11: Thank you
Questions?