## Slide 2: Team Members
Jacob Schofield - President
Nels Eide – Driveline / Testing
Mark Boeckmann - Engine
Keith Propson – Sound / Exhaust

## Slide 3: Team Goals / Vision
Fun, marketable snowmobile
85-horsepower class
Trail / touring category
Best Available Technology for sound
E-score above 195
17+ MPG

## Slide 4: 2016 Clean Snowmobile Challenge
20 Universities in Houghton, Michigan
Goal: Clean, Quiet, and Efficient
12th Overall
Award for Best Engine Design from Mahle Powertrain

## Slide 5: Build Comparison – 2016 vs. 2017
2016 Arctic Cat Pantera 3000
Kymco 700cc Twin
Haltech Elite 2500 ECU
Garrett Turbocharger
Cooled Exhaust Gas Recirculation (EGR)
Rear Exiting
Exhaust
Water to Air
Intercooler
Electronic
Throttle
MSRP: $12,692
2017 Arctic Cat ZR3000
Kymco 700cc Twin
Lightweight ZR Chassis
Advanced High-Flow EGR
Whisper-Drive System
Custom Intercooler Housed in Plenum
MSRP: $10,707

## Slide 6: Baseline Testing
Engine / Emissions
40.2 kW stock
E-score of approximately 191
Noise, Vibration, Harshness (NVH)
Completed J1161 test
35 mph steady state at 50 feet
72 dBa in stock trim
Competition goal is 67 dBa

## Slide 7: Engine Development
Ricardo WAVE Simulation
Low-pressure cooled EGR
  Venturi drawn
Turbocharged – Garrett MGT1238
Intercooled
  Integrated into intake plenum
Heraeus Catalyst
Electronic Throttle
Robust Control
  Haltech 2500 Elite

## Slide 8: Ricardo WAVE Simulation

## Slide 9: Dynamometer / Results
63 kW
Approximate E-score
of 201
Hydrocarbons (HC)
reduced 79%
Carbon Monoxide (CO) reduced 96%
Oxides of Nitrogen
(NOx) reduced 88%
Chart: NOx Emissions EGR Implemented
| -40 | -20 | 0 | 10 | 20 | 30 | 40 | 60 | 70 | 80
7500 | 254 | 430 | 858 | 754 | 140 | 193 | 115 | 160
7000 | 165 | 520 | 758.6 | 806 | 140 | 226 | 92 | 101
6500 | 212 | 380 | 628.5 | 811 | 140 | 140 | 94 | 80
6000 | 597 | 354 | 212.5 | 787 | 140 | 165 | 114 | 86
5500 | 748 | 547 | 408 | 583 | 140 | 413 | 100 | 190
5000 | 356 | 843 | 590 | 478 | 613 | 794 | 394 | 360 | 108
4500 | 120 | 57 | 32 | 54.7 | 203 | 98
4000 | 33 | 12 | 18.4 | 27 | 25
3500 | 47 | 130 | 442
Chart: NOx Emissions No EGR Implemented
| -40 | -20 | 0 | 10 | 20 | 30 | 40 | 60
7500 | 21 | 2700 | 1236 | 1800 | 2400 | 1590 | 390 | 210
7000 | 32 | 2800 | 1783 | 1900 | 2200 | 1386 | 405 | 200
6500 | 24 | 3100 | 1572 | 1700 | 1400 | 1509 | 303 | 190
6000 | 16 | 2600 | 2700 | 2400 | 1327 | 1580 | 100 | 240
5500 | 32 | 2500 | 2745 | 2200 | 1400 | 890 | 90 | 200
5000 | 40 | 2370 | 3337 | 1719 | 1230 | 1192 | 1142 | 1133
4500 | 120 | 295 | 360 | 420 | 508 | 609
4000 | 33 | 50 | 91 | 150 | 266
3500 | 6 | 650 | 758.5
3000 | 47 | 130 | 65

## Slide 10: Muffler Development / Design
Relocate muffler based on packaging constraints
Under-tunnel muffler retains factory appearance
Design based on anechoic chamber
3-chamber design
Closed cell frequency simulation

## Slide 11: Whisper-Drive System
Repurposed water-dyno for sound
10 hp electric motor with VFD
Driveline Sound Improvements
  Silent Drive track
  Removal of idler wheels
  Graphite filled hyfax
  Lizard Skin coating
5 dBa decrease in sound
emissions in test simulation

## Slide 12: On-Snow Calibration
Through extensive on-snow testing, drivability and reliability were greatly increased
Full clutch and E-Throttle calibration using Haltech data logging
Fuel-economy of 18
mpg on 91 octane
250 miles of validation

## Slide 13: Summary
Turbocharged engine with a 57% gain in power over stock, resulting in 63 kW
Cooled Exhaust Gas Recirculation system
70.6% decrease in NOx emissions
96% decrease in CO emissions
88% decrease in HC emissions
eScore of 201
Rear-exiting exhaust with a 4 dBa decrease in sound levels over stock
Calculated MSRP of $10,707

## Slide 14: Thanks!