## Slide 2: Vision
A new design cycle
Fun, marketable snowmobile
65 – horsepower class
Continue the practical, data-driven approach to innovation

## Slide 3: Team Management
Two-Year Design Cycles
Project Manager with individual Team Leads
Sophomores and Juniors hold leadership positions

## Slide 4: Innovations
Integration of the Polaris ProStar 1000 into the AXYS platform
Standalone MoTeC ECU
Electronic Throttle Control
Two-Chamber muffler design using destructive wave interference
Simulated Acoustic Imaging

## Slide 5: Engine Development
Polaris ProStar 1000
Ricardo WAVE Simulation
MoTeC M130 Standalone ECU
Electronic Throttle Control
Custom Intake and exhaust
3-way Catalyst

## Slide 6: Dynamometer / Results
45 kW (60 hp)
Hydrocarbons (HC)
reduced 92%
Carbon Monoxide (CO) reduced 97%
Oxides of Nitrogen
(NOx) reduced 73%

## Slide 7: Drivetrain Integration
Maintained factory mounting locations
Integrated the front engine mounts with the overstructure
Redesigned front crossbar to keep the center of gravity of the snowmobile low

## Slide 8: Drivetrain Integration
Double U-Joint steering system
Steering uses 5 separate mounts on the overstructure while maintaining relatively factory steering angle
1020 steel spars designed to accommodate the intake and fuel system

## Slide 9: Muffler Development / Design
Dominant Frequency identification
Quarter wavelengths were used to dictate muffler design
Two chamber design
Destructive wave interference
Baffles and resonator tubes targeting dominant frequencies

## Slide 10: Simulated Acoustic Imaging

## Slide 11: Sound Dyno
Repurposed water-dyno for sound
10 hp electric motor with VFD
Driveline Sound Improvements
  Rear Shrouding
  Removal of idler wheels
  Graphite filled hyfax
  Lizard Skin coating
  Anti-Stab wheels
6 dBa decrease in sound
emissions in test simulation

## Slide 12: On-Snow Calibration / Testing
Through extensive on-snow testing, drivability and reliability were greatly increased
Full clutch and E-Throttle calibration using MoTeC data logging
Fuel-economy of 13
mpg on 91 octane
J1161 of 71.8 dBa
150 miles of validation

## Slide 13: Summary
45 kW enjoyable trail snowmobile
80%+ reduction in emissions
6 dBa decrease in chassis sound emissions
J1161 test of 71.8 dBa
MSRP of $11,766
Well designed platform for the future.

## Slide 14: Thanks!