## Slide 1: TEAM QUIETS-DUC 2017 SAE CSC DESIGN PRESENTATION
By: Dominic Mathieu and Guillaume Verner

## Slide 2: Presentation content
Overall packaging
Chassis modifications
Drivetrain modifications
Powerplant
Other modifications
Testing
Notes: Do

## Slide 3: Overall packaging
Objective : Marketable work snowmobile
Ski-Doo Tundra Sport
Kohler KDW1003
Notes: Do

## Slide 4: Chassis modifications
New S-module design
Simulated at 765 lbs
Notes: Gui

## Slide 5: Chassis modifications
Steering column redesign
Notes: Gui

## Slide 6: Powerplant
Stock engine specifications :
  Inline 3 cylinders
  1028 cc
  Mechanical fuel injection
  23.4 HP
  36.8 ft-lbs
Current engine specifications* :
  30 HP
  46 ft-lbs
* Based on dyno run at CSC 2017
Notes: Do

## Slide 7: Powerplant
Turbo selection : Garrett MGT1238
Notes: Do

## Slide 8: Powerplant
Exhaust design :
  DOC/DPF
  Muffler
Notes: Do

## Slide 9: Powerplant
Flywheel alternator
Notes: Do

## Slide 10: Drivetrain modifications
Clutches :
  Specially designed
  for our application
  Operating range :
  900 to 3600 RPM
  Driving ratio :
  4:1 to 0.75:1
  Heavier weights
  and stiffer spring
Notes: Gui

## Slide 11: Drivetrain modifications
Drive sprocket Chaincase ratio
Bottom chaincase gear:
  Stock : 51 tooth
    Top Speed = 45 mph
    RPM @ 35 mph = 3000
  New : 43 tooth
    Top Speed = 55 mph
    RPM @ 35 mph = 2500
Notes: Gui

## Slide 12: Other modifications
Heat management
Soundproofing
Stiffer front springs
Battery
Notes: Gui

## Slide 13: Testing
Air Fuel Ratio at :
  Full load & full throttle : 17.5 : 1
  Trail speed (35 mph) :
  25 to 30 : 1
Notes: Gui

## Slide 14: Questions?