## Slide 1: TEAM QUIETS 2017 SAE CSC DESIGN PRESENTATION
By:
Marc-Antoine Fitzgerald
Édouard Levesque

## Slide 2: Presentation content
2017 HPDI 600 ACE
Noise Reduction
Drivetrain efficiency increase
Conclusion

## Slide 3: HPDI
High pressure direct injection design
Parts needed:
DI injectors
High pressure fuel pump
Modified pistons
Motec M142

## Slide 4: HPDI
DI injectors
Bosch model: 0 261 500 162 (found on VW 2.0 TSI)
Programming requirements:
Spray pattern
Injection curve

## Slide 5: HPDI
Injection pattern
Required for cylinder head drilling and pistons design

## Slide 6: HPDI
Injection curve

## Slide 7: HPDI
High pressure mechanical fuel pump
Pump model: Hitachi HPP0004 (found on VW 2.0 TSI)
Pressure range: 500-2500 PSI
Optimized cam lobes for flow requirement

## Slide 8: HPDI
DI optimized piston shape
Optimized shape for injector angle and clearance
Maximize fuel atomization
Prevent cylinder wall wetting

## Slide 9: HPDI
New cylinder head design
Modified head to install DI injectors

## Slide 10: HPDI
Motec M142 ECU
V.E. (Volumetric efficiency) engine based map

## Slide 11: Dyno and Emissions Control
Catalytic converters
Equal length individual exhaust tubes
Pre-cat wide bands
After cat narrow bands

## Slide 12: Noise Reduction
Big wheels and track

## Slide 13: Noise Reduction
New drive gear design
9 tooth design
Constant contact point
Rotating drive rollers
Separate hub from sprocket
-4% amp draw

## Slide 14: Noise Reduction
Big wheels and track
Modified track structure
8’’ plastic/rubber big wheels (-1dB from aluminum to rubber big wheels)
Chart: Return wheels comparison
| 1200.0 | 1800.0 | 2400.0
OEM wheels | 1.5 | 3.15 | 6.45
Alu. Big wheels | 1.3 | 2.85 | 6
Rubber big wheels | 1.3 | 2.8 | 5.95

## Slide 15: Conclusion
MXZ Blizzard 600 ACE Turbo
Same power plant as last year
Slightly modified tune

## Slide 16: Questions?