## Slide 1: TEAM QUIETS #04 École de technologie supérieure 2019 SAE CSC DESIGN PRESENTATION
By:
Mathieu Verner
Quentin Gravel

## Slide 2: Presentation content
600 ACE turbo
Noise and efficiency
Additional features

## Slide 3: 600 Ace Turbo
New turbo location and exhaust manifold
2018
2019

## Slide 4: 600 Ace Turbo
Intercooler

## Slide 5: 600 Ace Turbo
Steering column

## Slide 6: 600 ACE Turbo
E20.2
79.5 hp
60.3 ft.-lbs
BSFC : 490 g/kW-hr
2018 specifications
87 octane
90 hp
68.3 ft.-lbs
BSFC : 490 g/kW-hr
2019 specifications (estimations)

## Slide 7: 600 ACE Turbo
Catalytic converter
  Larger diameter
  Better flow
  Lower emissions

## Slide 8: Noise and efficiency

## Slide 9: Noise and efficiency
Big wheels and track
  Modified track structure
  8” plastic/rubber big wheels
  15% amperage draw reduction
Chart: Return wheels comparison
| 1200 | 1800 | 2400
OEM wheels | 1.5 | 3.15 | 6.45
Alu. Big wheels | 1.3 | 2.85 | 6
Rubber big wheels | 1.3 | 2.8 | 5.95

## Slide 10: Noise and efficiency
Custom drive sprocket design
  9 tooth
  Constant contact
  Drive rollers
  4% amperage draw reduction

## Slide 11: Additional features
Roller ski
  Auto retractable ski wheel system
Reverse
  Because every snowmobile should have a reverse
Ice scratcher
  Lubricate the track clips to reduce friction
  Reduce coolant temperature on icy conditions
Adjustable ski runner depth
  Adapt to all snow conditions
3D printed can holder!
  Coca-Cola and Redbull version available

## Slide 12: Questions?