## Slide 1: 2018 SAE Clean Snowmobile Challenge Design Presentation
Ferris State
Clean Snowmobile

## Slide 2: Overview
Team Goals
Design Process
Fuel Management
Muffler
Catalytic Converter
Other Modifications
MSRP

## Slide 3: Team Goals
Qualify for CSC 2018
Complete All Events
Prove Reliability
Improve Noise Quality
Reduce Emissions
Maintain Rider Experience
Learn from Mistakes

## Slide 4: Design Process
2017 SAE CSC Visit
Polaris Sled Donation
Formation of Project Groups
Design and Simulations
Fabrication
Testing
2018 SAE CSC

## Slide 5: Fuel Management
Ethanol Sensor
Engine Tuning

## Slide 6: Fuel Management
Strategy
  Lean AFR Targets
    Too Lean Causes Knock
      Engine Enters Limp Mode
  1.05 for Efficiency
  1.2-1.3 for Emissions
    Unrealistic for a 2-Stroke
  Much More Research Needs to be Done

## Slide 7: Fuel Management
Lambda (Assuming Stock Map at Pure Stoich) |  |  |  |  |  |  |  |  |  |  | 
 |  | Throttle Position (%) |  |  |  |  |  |  |  |  | 
 |  | 0 | 2 | 5 | 10 | 15 | 20 | 40 | 60 | 80 | 100
Engine RPM | 500 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
 | 750 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
 | 1000 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
 | 1250 | 1.15 | 1.15 | 1.00 | 1.00 | 0.97 | 0.94 | 0.91 | 0.91 | 0.91 | 0.91
 | 1500 | 1.15 | 1.15 | 1.00 | 1.00 | 0.94 | 0.91 | 0.88 | 0.88 | 0.88 | 0.88
 | 1750 | 1.15 | 1.15 | 1.09 | 1.00 | 0.91 | 0.88 | 0.85 | 0.85 | 0.85 | 0.85
 | 2000 | 1.15 | 1.15 | 1.09 | 1.00 | 0.94 | 0.91 | 0.88 | 0.85 | 0.85 | 0.85
 | 2250 | 1.15 | 1.15 | 1.15 | 1.09 | 1.00 | 0.94 | 0.91 | 0.88 | 0.85 | 0.85
 | 2500 | 1.15 | 1.15 | 1.15 | 1.09 | 1.00 | 0.97 | 0.91 | 0.91 | 0.88 | 0.85
 | 2750 | 1.09 | 1.12 | 1.15 | 1.15 | 1.09 | 1.00 | 0.94 | 0.91 | 0.91 | 0.88
 | 3000 | 1.09 | 1.12 | 1.15 | 1.15 | 1.09 | 1.00 | 0.97 | 0.94 | 0.91 | 0.91
 | 3250 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15 | 1.09 | 1.00 | 0.94 | 0.94 | 0.91
 | 3500 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.09 | 1.00 | 0.97 | 0.94 | 0.94
 | 3750 | 1.06 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15 | 1.09 | 0.97 | 0.97 | 0.94
 | 4000 | 1.06 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.09 | 1.00 | 0.97 | 0.97
 | 4250 | 1.00 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15 | 1.00 | 1.00 | 0.97
 | 4500 | 1.00 | 1.06 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.09 | 1.00 | 1.00
 | 4750 | 1.00 | 1.06 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15 | 1.09 | 1.00
 | 5000 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.12 | 1.15 | 1.15 | 1.09 | 1.00
 | 5250 | 1.00 | 1.00 | 1.06 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15 | 1.09
 | 5500 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15 | 1.09
 | 5750 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.09 | 1.15 | 1.15 | 1.15 | 1.15
 | 6000 | 1.00 | 1.00 | 1.00 | 1.00 | 1.09 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15
 | 6250 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.15 | 1.15 | 1.15
 | 6500 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.12 | 1.15 | 1.15
 | 6750 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.15 | 1.15
 | 7000 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.15 | 1.15
 | 7250 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.12
 | 7500 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12 | 1.12
 | 7750 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12
 | 8000 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09 | 1.12
 | 8250 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09
 | 8500 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06 | 1.09
 | 8750 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06
 | 9000 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.06
 | 9250 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
 | 9500 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00 | 1.00
Mode 1
  Very Poor
    Limp Mode
Mode 2
  Good
Mode 3
  Good
Mode 4
  Good
Mode 5
  Poor

## Slide 8: Custom Muffler
Shell Development
  Original volume conservation with addition of catalyst
  Ease of fabrication
Internal Geometry
  Designs simulated to predict best Insertion Loss

## Slide 9: Simulations
Attenuation Targets High Frequencies
  Above 500 Hz
  Unpleasant to Human Ear
Perforate Location on Pipes Optimized for High Frequencies

## Slide 10: Final Design
Sound Cancelling Geometry
  Perforated Baffle
  Perforated Pipe
  3.56 dBA Reduction on Average
    Above 500 Hz

## Slide 11: Emissions Treatment
Rationale
  Cost Effective
  Feasibility
Design Considerations
  Space Constraints and Heat
    Dissipates Heat Quickly
    Durable Against Mechanical Vibrations
  Backpressure
    Low Cell Density
  Emissions

## Slide 12: Stock and Custom Flow Comparison
Flow characteristics were a primary consideration so that engine performance and operation were not drastically effected

## Slide 13: Simulated Backpressure
Stock:
95.1 kg/hr
New System:
86.1 kg/hr

## Slide 14: Emissions
Average Percent Difference:
92.2% decrease in HC, 87.0% decrease in NO,
58.4% increase in CO₂ , and a 61.6% decrease in O₂

## Slide 15: MSRP
Component | Cost | Comments
Stock Sled | $13,999 | 
Muffler | $1,200 | Estimated including hourly wage of welder
Catalyst | $97.71 | 
Ethanol Sensor | $349 | 
Traction Studs | $228 | 
Runners | $60 | 
Resonator Removal | (-703.99) | PN: 1262701
Total | 15,299.72 | 

## Slide 16: Lessons Learned
AFR is too Lean
  Run Closer to Stoich
Improve Catalyst Insulation Method
Tune Suspension for Improved Handling
Use Emissions Data to Improve Catalyst Substrate
Perform Engine Dyno Tests Before Competition

## Slide 17: Thank You Sponsors
College of Engineering and Computing Technology Dean’s Office

## Slide 19: 2018 SAE Clean Snowmobile MSRP Presentation
Ferris State
Clean Snowmobile

## Slide 20: Overview
Stock Sled
Custom Muffler
Catalytic Converter
Ethanol Sensor
Traction Control
Deleted Parts

## Slide 21: Stock Sled
2017 Polaris 800 Switchback Assault 144
  $13,999

## Slide 22: Muffler
Wholesale Cost
  304 Stainless Steel and Heat Wrap
    $300
  Welding Man-Hours
    $500
Retail Cost
    $800 x 1.5 Multiplier
    $1200

## Slide 23: Catalyst
MagnaFlow Universal Spun Catalyst
  Metallic Substrate
  200 CPI
  $97.71

## Slide 24: Ethanol Sensor
Zeitronix ECA-2
  Heads-up Display
$349

## Slide 25: Traction Control
Studs
  $228
Runners
  $60

## Slide 26: Stock Resonator Removal
AXYS Resonator
  (-$703.99)
    PN: 1262701

## Slide 27: Total
Component | Cost | Comments
Stock Sled | $13,999 | 
Muffler | $1,200 | Estimated including hourly wage of welder
Catalyst | $97.71 | 
Ethanol Sensor | $349 | 
Traction Studs | $228 | 
Runners | $60 | 
Resonator Removal | (-703.99) | PN: 1262701
Total | 15,299.72 | 

## Slide 28
Questions?