## Slide 1
Presented By:
Jared Kellerer,
Steven Gasseling
Notes: STEVE

## Slide 2: Overview
Project management
UICSC goals & platform
Past work
Engine and sound testing
Silent Drive & Silent Track
Notes: STEVE

## Slide 3: Team management
structure
Faculty Advisor
Graduate Students
Alumni
Senior Captain
Junior Captain
Upperclassmen
New Members
Notes: STEVE
The team structure

## Slide 4: Team management
Project Management
Gantt Chart
  Effectively tracked large projects
  Difficult to maintain accountability
Kanban Method
  Promotes individual accountability
  Increased small team progress monitoring
To Do
In Progress
Completed
Notes: Steven
Gantt
Strengths: Good for managing timeline of multiple projects macro scale
Weakness: fine project management, small team, individual, not as well
Kanban
Strengths: Promotes individual accountability, and small scale progress monitoring
Downside: Implementing a new method of management can be unfamiliar and we are still learning how to use it

## Slide 5: Team management
Course
Curriculum
  CSC introduction
  Engineering topics
  Professional development
Student led
  Presentations by senior members
Notes: STEVE
Major overhaul carried out by senior
Using knowledge of senior team members
Presentations

## Slide 6: UICSC Goals
Produce an NPS certified two-stroke
  E-Score > 175
  Sound output < 67 dBA
Fun to ride
Improved testing & validation
Notes: STEVE
As always the UICSC strives to…
Fun to ride AND marketable

## Slide 7: UICSC Platform
2017 Ski-Doo MXZ TNT
REV GEN4 Chassis
850 E-TEC Engine
Notes: STEVE
Produce an NPS certified two-stroke
  E-Score > 175
  Sound output < 67 dBA
Fun to ride
Improved testing & validation

## Slide 8: Prior modifications
Reduced engine speed
3 way catalyst
Sound material
  Absorption
  Damping
Increased diameter rear idler wheels

## Slide 9: Engine calibration
Maintain survivability
Minimize emissions
Target BSFC in appropriate areas
Swept parameters
  Fuel injection timing
  Fuel injection quantity
  Throttle body/E-TEC ratio
  Ignition timing

## Slide 10: Snowmobile Design
Prior work
  Reduced engine speed
    6850 RPM
    118 hp
  Extended tuned pipe
    Optimized length for BSFC
    Empirical calculation and simulation
  3-way catalyst
    1:20:1 Platinum:Palladium:Rhodium
    Dual substrate
Notes: JARED
Downsped large displacement on basis of reducing sound production in J1161 with lower engine speed and smaller throttle angle than small displacement
At reduced engine speed, trapping pulses no longer timed correctly. To determine new length, used empirical and GT simulation.
1201 ppr at exit of muffler to reduce emissions
Reduced speed 850 to produce similar power to a 600. Our theory: during j1161, lower engine speeds > lower frequencies produced by engine (A weight); reduced throttle opening > lower exhaust pressures (reduce amplitude of sound produced)
Use 850, stock: produces significantly more than competition limit of 130 hp. We downspeed the engine to meet comp requirements and approximately match the performance of a 600 cc engine. Running a downsped 850 provides a few advantages over just a 600. the lower engine speeds required to produce similar output result in reduced sound pressure measured on the A-weighted scale. At common cruise speeds, we are able to shift the operating range of the engine to more efficient areas
Focus on explaining why we use an large displacement engine
sound -> we see reduced dBA with reduced engine speed
efficiencies -> shift engine operation to more efficient points

## Slide 11: Snowmobile Design
Prior work
  Tunnel sound damping
    Damping ratio
    Polymer Technologies Silent Running
  Sound absorption
    Power transmission coefficient
    Polymer Technologies Melamine 3-Layer foam
  Increased diameter idler wheels
    Reduced dynamic rolling resistance
    Facilitate new track
Damping ratio:
Notes: JARED
Sound produced by tunnel vibrations is addressed with damping material. Various matls tested to determine silent running had the best damping ratio – applied.
Sound from the engine and cvt is attenuated with absorption material. Melamine 3 layer found to have best ptc, applied.
BWK yielded reduced dynamic rolling resistance and allows use of new track

## Slide 12: Innovations
In-service testing
ECU data collected during operation
Influences calibration and design
Examples
  Engine operating point frequencies
  Calculated fuel consumption
  Track & engine speed
Notes: JARED
Engine frequency -> BSFC focal areas in calibration
MPG -> efficiency testing, e.g. Silent Track II
Track/Engine speed -> Acoustic testing, clutch: as aftermarket components became available for P Drive, able to test & tune with in-service data (speeds as well as fuel consumption)

## Slide 13: Innovations
Dynamometer updates
Improved data acquisition
  Centralized
  Time synchronous
  Time averaged
Ramped Modal Cycle testing
  Replicating CSC environment
  Evaluating transient performance
Notes: JARED
State that we aren’t yet using this to its fullest potential

## Slide 14: innovations
Combustion analysis
In development
Goals
  In-cylinder pressure
  IMEP & PMEP
  Mass fraction burned
Volume
Pressure
Crankshaft Angle from TDC
MFB
50%
Taken from: Robert Hickling, Douglas A. Feldmaier, Francis H. K. Chen, et al., “Cavity Resonances In Engine Combustion Chambers And Some Applications” The Journal of the Acoustical Society of America 74, no. 4 (1983): 1171
Notes: JARED
McCuiston, Lavoie and Kauffman (MLK) model
With IMEP and PMEP, calculate frictional losses
Use mfb to determine appropriate spark timing at different operating points
Gamma – ratio of specific heats
N – polytropic exponent, 1.3 for conventional fluids
MFB plot, Blair pdf pg316
See knock, IMEP discussion, CA10,50,90
Equipment
  0.35° encoder
  Head mounted pressure transducer
  Crankcase absolute pressure sensor
  High speed DAQ

## Slide 15: innovations
Order analysis
Identifies major sources of noise
Vibration data
Process
  Decompose signal
  Determine order
  Relate order
  Address
Notes: STEVE

## Slide 17: Innovations
Track
Ski-Doo Silent Drive & Silent Track II implemented
  Irregular contact pattern
  Plastic-rubber contact
Results
  0.9 dBA reduction from 2018 configuration
  8% decrease in roll-out distance
Notes: JARED
What track did we run in 2018?
69.2
Rollout data in aux slides
Reference slide: paper for acoustic impact response

## Slide 18: results
 | Stock | 2019 UICSC
E-Score | 133 | 180
J1161 Sound Pressure | 70 dBA | 67.7 dBA
Fuel Consumption | 13.8 mpg | 18.6 mpg (+35%)
Power | 165 hp | 118 hp (-28%)
Notes: JARED

## Slide 19: Thank you to our sponsors
Dr. Dan, Dr. Hess, Dr. Anderson, Dr. Beyerlein, Rob Patton, Bill Magnie

## Slide 20: Auxiliary slides

## Slide 22: innovations
Sound vectoring
Identify areas of noise production
Improved data processing
Notes: STEVE
The UICSC team can only address noise if we know where its coming from.
Sound vectoring is the process we have used in the past and continue using because it offers a
relatively unbiased picture of where sound is being produced on our chassis.
Testing procedure:
Our testing procedure as remained unchanged as well
We place a wire grid is 3ft away, snowmobile run on a stand at 4100 rpm (similar speed as seen in J1161)
A control mic is placed at the center, with 16 outer points measured with a test mic
Allowig us to
Innovation
Previously we could only look at one frequency at a time, due to our data processing. (notes into excel into matlab, back into excel)
This year we focused on more accurately representing insertion loss over frequencies from 86 to 21946 Hz (essentially, the range of human hearing)
Superimposed all the data on one image
Pictures
These are the photos resulting from the entire frequency spectrum (up to 21000 Hz)
And interpolated between the points

## Slide 23: Sound Material Testing
Anechoic Sound Box Results
Power transmission coefficients
Best: Melamine Three Layer

## Slide 24: GT Suite: Tuned Pipe Model

## Slide 25: GT Suite Specifications
Engine speed | 6800 RPM
Optimization method | Local minima
Design variable | Dwell length
Factor range | -10 to 20 cm [-3.9 to 7.9 in.]
Output variable | BSFC
Resolution | 0.3 cm [0.1 in.]

## Slide 26: Catalyst Comparison
  Blank and coated catalysts of two styles were compared
  Used dual substrate with three-way 1:20:1 Platinum:Palladium:Rhodium coating
  Tested E-score of 180
Catalyst | E-score
Stock/No Catalyst | 133
Blank Single | 141
Blank Dual | 149
1:20:1 Single | 165
1:20:1 Dual | 180

## Slide 27: Damping Material Testing
Damping Ratio Results
Material | Average Damping Ratio
Bare aluminum | 0.010
PolyDamp single side | 0.034
PolyDamp both sides | 0.045
Silent Running single side | 0.063
PolyDamp + Silent Running | 0.082
Silent Running both sides | 0.142

## Slide 28: Larger Rear Idlers
10 in. idler wheels for improved efficiency
Multiple configurations tested
Configurations

## Slide 29: Larger Rear Idlers
Testing Results
Component | Roll-Down Angle (°)
Stock idler wheels | 11.4
4 large idler wheels | 11.5
3 large idler wheels | 11.6
2 large idler wheels | 12.2
Tested Component | Roll-Out Distance (m [ft]) |  | 
 | 80 kmph [50 mph] | 64 kmph [40 mph] | 48 kmph [30 mph]
Stock idler wheels | 94.8 [311] | 62.2 [204] | 43.9 [144]
4 large idler wheels | 95.1 [312] | 69.2 [227] | 44.8 [147]

## Slide 30: ReferenceS
Metal vs Plastic Impact
Sarlin, E., Liu, Y., Vippola, M., Zogg, M., Ermanni, P., Vuorinen, J., & Lepistö, T., “Vibration damping properties of steel/rubber/composite hybrid structures.” Composite Structures, (94), 3327-3335. DOI: 10.1016/j.compstruct.2012.04.035