## Slide 1: Iowa State University
2016 Clean Snowmobile Challenge

## Slide 2: Agenda
Chassis Selection
Chassis Improvements
Exhaust Treatment
Engine Calibration
Questions

## Slide 3: Chassis Selection
2014 Polaris Indy 800SP
795cc Cleanfire Liberty 2-stroke
Aluminum ProRide Chassis

## Slide 4: Chassis Selection
Buyer brand preference
Chart: 
| Arctic Cat | Polaris | Skidoo | Yamaha

 | 0.12195 | 0.58537 | 0.17073 | 0.12195

## Slide 5: Chassis Selection
Buyer engine displacement preference
Chart: 
| 1000cc and up | 800cc-999cc | 600cc-799cc | Below 599cc

 | 0.097561 | 0.36585 | 0.43902 | 0.097561

## Slide 6: Chassis Selection
Importance of fuel economy to buyers when purchasing snowmobile
Chart: 
Very Unimportant | 0.11905
Unimportant | 0.21429
Moderate Importance | 0.40476
Important | 0.2381
Very Important | 0.02381

## Slide 7: Chassis Improvements
Sound Deadening Material:
RAAMmat BXT II
Placed in engine bay
Significantly reduced noise levels from engine

## Slide 8: Chassis Improvements
Chart: 
| Boondocking | Groomed Trails | Ungroomed Trails
 | 0.17073 | 0.43902 | 0.39024
Buyer riding conditions preference

## Slide 9: Chassis Improvements
Track Selection:
Ripsaw 1.5
1.5” lugs
96 1-5/8” Woody’s Traction Studs

## Slide 10: Exhaust Treatment
Emission Analysis of 2-stroke oils:
Five oils analyzed
Test run by intervals of 500rpm between 3000rpm and 5000rpm
Oil system flushed between samples

## Slide 13: Exhaust Treatment
Amsoil Interceptor proved to be best candidate
Oil Name | Definite Integral (Cumulative % over 110 seconds) | Percent Increase Compared to Lowest
Interceptor | 191.884 | N/A
Polaris VES | 202.515 | 5.25%
Dominator | 203.008 | 5.48%
Klotz | 229.758 | 19.74%
G-Oil | 205.375 | 7.03%
Oil | Definite Integral (HC parts per million cumulative over 110 seconds) | Percent Increase Compared to Lowest
Interceptor | 601,577 | N/A
Polaris VES | 662,111 | 10.06%
Dominator | 780,694 | 29.77%
Klotz | 629,608 | 4.66%
G-Oil | 644,463 | 7.13%
Hydrocarbons
Carbon Monoxide

## Slide 14: Exhaust Treatment
Catalytic Converter:
400cpsi Heraeus catalyst
Targets constituents of carbon monoxide and excess hydrocarbons
Composition
  Platinum, Palladium, Rhodium (1:20:1)

## Slide 15: Exhaust Treatment
Sound Treatment:
Twin high-flow mufflers
Stainless steel wool packing for heat resistance
Manufactured primarily for space restrictions and catalyst installation

## Slide 16: Engine Calibration
Engine Management:
Power Commander V (PCV)
  Fuel Mapping
  Ignition timing
GM Flex Fuel Sensor
  Ethanol compensation
  0-5V signal to PCV

## Slide 17: Engine Calibration
Adjustment to catalyst:
First catalyst struggled with short-circuited fuel
Adjusted system to move catalyst further downstream
Progressive tune implemented
Throttle Position (% Open) | Target Lambda Value
0-40 | 1.3
41-60 | 1.1
61-80 | 1.0
81-100 | 0.9

## Slide 18
Questions?