## Slide 1
Iowa State Clean Snowmobile Challenge
2017

## Slide 2
Overview
Snowmobile Selection
Traction
Sound
Exhaust
Tuning
Oil Selection

## Slide 3
Snowmobile Selection
2015 Polaris 600 Rush Pro-X
  Trail rider
    Engine displacement
    Handling
  Reliability
    600 Liberty

## Slide 4
Traction
120 x 1.25” Ripsaw II Track
1.325” 60˚ carbide tip Gold Digger studs
84 single pattern
  Reduced to 42 for weight minimization

## Slide 5
Sound
Two primary materials tested
  Linex (1/16” and 1/8”)
  Raam Matting
  Ensolite foam tested as a complementary treatment
Analyzed at 3 frequencies
  1000 hz (High)
  600 hz (Mid)
  200 hz (Low)
1/8” Linex with Ensolite Foam chosen
Notes: High- 93.5 Dba
Mid- 84.7 Dba
Low- 75.6 Dba

## Slide 6
Sound
Notes: High- 93.5 Dba
Mid- 84.7 Dba
Low- 75.6 Dba

## Slide 7: Exhaust
Destructive interference
  Reduce sound pressure levels
Chosen over an absorptive muffler
Flow simulation conducted
  Ensure proper flow
  Validate exhaust gas velocity
Notes: Reactive is more restrictive, but still is able to reduce sound levels
To run the flow simulation we calculated the theoretical mass flow rate by using engine displacement, engine RPM, and volumetric efficiency of 65% - two stroke.

## Slide 8
Emissions
Implemented 2 catalysts
  3-way catalysts
  200 cells per square inch
Palladium and Rhodium coating filters out
  HC
  CO
  NOx
Lean Tune
  Oxidize HC and CO
Notes: Main emissions harmful to environment.

## Slide 9
Tuning Hardware
Power Commander V
Zeithronix Ethanol Analyzer
NGK Afr Gauge

## Slide 10
Perfect stoich - 1.00 Lambda
Idle/Cruise - 1.08 Lambda
WOT (wide open throttle) - 0.87 Lambda
Tuning Strategy

## Slide 11
Oils
Carbon Monoxide
Hydrocarbon

## Slide 12
Questions?