## Slide 1: Iowa State University Clean Snowmobile Challenge

## Slide 2: Agenda
Season Summary
Accomplishments
  Testing
    Baseline
    Cold Start
  Innovations
Areas of Improvement
  Timeline Management
  Team Lead Positions

## Slide 3: Season Summary
  Snowmobile: 2018 Arctic Cat ZR 7000 Sno Pro
  Strategy: Prioritize reducing noise pollution
  Approach:
    Research potential projects
    Solidify season project(s)
    Conduct baseline testing
    Design innovations
    Manufacture & Implement innovations
    Conduct final testing

## Slide 4: Baseline Testing - Noise
Procedure: SAE J116
Instrumentation: MTS Systems sound meter
Results: target range of 31.5 - 1000 Hz

## Slide 5: Baseline Testing - Emissions
Procedure:
EPA 40 CFR Part 1051 (Ramped Modal Cycle)
Instrumentation: Bridge 5 gas analyzer
Results:
Calculated E-Score: 120.65

## Slide 6: Cold Start Testing
Procedure:
Test 3 days consecutively
Day 1 = -10
Day 2 = 0
Day 3 = 10
Results:
Faulty stock battery –
75% charge, 280/310
total crank amps

## Slide 7: Innovations
Exhaust
  Mufflers
  Pipe routing
  Catalyst
  Heat shielding
Additional bogey wheels
  3D printed support arm
ECU
  G4+ Link Fury
  Throttle Body Restrictors

## Slide 8: Mufflers

## Slide 9: Pipe routing, Catalyst, Heat shielding
304 Stainless Steel
45 & 90 degree mandrel bends,
straight section
Custom bent section
Flanges & gaskets
Aristo Intelligent Catalyst Technologies
3-way oxidation with inner proprietary coating
Pipe Routing
Catalyst
Heat Shielding
Full contain design
16 ga. mild steel
2300 ceramic heat blanket
Heat wrap

## Slide 10: Additional Bogey Wheels
3D printed upper tension arm
Printed at Viking Pump with Markforged 3D printer
chopped carbon fiber (“Onyx”)
& reinforced fiberglass
Additional set of bogey wheels on lower skid rail

## Slide 11: ECU
G4+ Link Fury
Complete stand alone
Custom wiring harness

## Slide 12: Time Line Management
October 14th - Initial baseline testing
completed
October 20th - Begin innovation design and
integration
December 17th - Final design selected for
additional team designed muffler
January 19th - Begin ECU tuning
February 3rd - All innovations fully
integrated
and tuned, sled is competition ready

## Slide 13
Iowa State SAE
Project Director
Engine Team Lead
Exhaust Team Lead
Testing Team Lead
Tech Director
Chassis and Suspension Team Lead
Outreach Team Lead
Safety Officer
Team Lead Positions
New positions to incorporate
Selection based off of passion and available time rather than knowledge

## Slide 14: Citations
SAE International. “2019_SAE_CSC_rules_FINAL_Draft_10.5.2018.Pdf.” SAE International, 2018.