## Slide 1: Development of Zero Emission, Electric Snowmobile
Indiana University Purdue University, Indianapolis
Team : Avinash Mumabraddi, Mohammed Alsigoor, Abdullah, Ahmed, Natasha Hunter

## Slide 2: Overview
Introduction
Operator Perspective
Dealer Perspective
Environmental Perspective
Results
Conclusion
Questions

## Slide 3: Introduction
Phase 2
2nd year modifications of 2015 Polaris Indy 550 snowmobile
New Battery Box
New Enerdel commercially made battery pack
3D printed parts
Carbon Sled MonoSuspension

## Slide 4: Operator Perspective
North/South Slope users
  Need efficient and clean vehicles for short trips for core sample collection.
  Range estimated of over 10 miles with 3KWhr pack.
  Battery box designed for 6KWhr pack … for a better range of 20 miles.
  Maximum speed of 40 mph, which is not a major need
  The ergonomics of the snowmobile has one major modification of the seat being on top of the battery box. It would be appropriate for short trips.

## Slide 5: Dealer Perspective
Design is simple with off the shelf components:
  Battery, Enerdel
  Battery Charger
  BMS
  Curtis 1238 controller
  AC-9 Motor
  MSRP= $16K (with 10 mile range)
  Or $19K (with 20 mile range)
  No major modifications, except battery box, and direct drive belts.
  Easy to start and drive
  Effort to make a comfortable seat, and keep driving posture unmodified

## Slide 6: Results
Maximum battery size of 8KWhr.
Decided to use 3KWhr to decrease weight and costs and obtain 10 mile range.
Battery capacity = 32 Ahr x 96 v = 3.072 KWhr
Efficiency loss of 20% = 2.457 KWhr
Estimated power is 204W/mi produces 12 miles.
Since F= rr(v)(m) , rr is a major of factor overall range.
Total range = 11.8 miles

## Slide 7: Conclusion
Snowmobile Met design goals for this competition
Around 40 lbs of weight reduction over the past year
Components and wiring were improved over the pervious year
Testing was completed to discover and eliminate weak portion of the design

## Slide 8: Question