## Slide 1: Kettering University
Development of a Flexible Fueled Snowmobile for the 2015 SAE Clean Snowmobile Challenge

## Slide 2: Design Approach
Versatility
  Performance 60 hp class snowmobile
  All around heavy hitter
  Mode switch optional
Advanced Controls
  Electronic Throttle
  Custom engine code
  Infinite flexibility
Noise Attenuation
  Affordable, lightweight silencer with acoustic valve
  Automotive grade sound deadening material
4. Emissions
  Three way catalyst with application-specific washcoat
  Extended lean-burn calibration
5. Dynamic Performance
  Performance increase over OE model with turbocharged power
  Light-weight
  Adaptable to riders, dealers, and outfitters

## Slide 3: Kettering 2015 Skidoo MXZ Sport

## Slide 4: Late Intake Valve Closing
Simulation DOE shows most efficient:
  20 degree intake cam retard from OE
  Increasing intake charge pressure
Exhaust camshaft as intake cam: LC 126 ATDC, IVC 61 ABDC
Turbocharger provides intake charge pressure for efficiency and power

## Slide 5: Compressor Matching
Honeywell Garrett MGT1446Z turbocharger
  Larger than traditional compressor match
  Odd-fire twin cylinder engine with large exhaust pulses
  Large turbine wheel and housing for low backpressure

## Slide 6: Miller Cycle 600 ACE Engine
Stock 12:1 compression ratio to preserve efficiency
Late intake valve closing for reduced pumping losses
Increased torque with turbocharger boost
Decreased modal BSFC from stock naturally aspirated
Improved vehicle performance—appeals to more riders
Chart: Emissions Mode BSFC--E65 fuel
| Mode 4 | Mode 3 | Mode 2 | Mode 1
Series 3 | 3 | 2 | 2
Turbo Miller Cycle | 423 | 367 | 350 | 360
Stock N/A | 544 | 400 | 346 | 335

## Slide 7: Dynamic Performance--Light Weight
546 lb with fluids, without fuel
Second lightest snowmobile at CSC 2015
Launch and traction control for acceleration and handling
Cost-effective at estimated $10,000 MSRP
An efficient, quiet, low-emissions performance trail sled to enjoy in fast company!

## Slide 8: Thanks to our 2015 Sponsors!