## Slide 1: Kettering University
Development of a Flexible Fueled Snowmobile for the 2016 SAE Clean Snowmobile Challenge

## Slide 2: 2016 Design Approach
Versatility
  Performance 70 hp class snowmobile Miller cycle engine for high efficiency and performance
Advanced Controls
  Full Authority Engine Management
  Electronic Throttle
  Custom engine code
Noise Attenuation
  Affordable, lightweight silencer with acoustic valve
Emissions
  Extended Lean-Burn Operation
  Lean NOx Trap Catalyst
Dynamic Performance
  Performance increase over OE model
  Lightest weight without fuel at CSC 2014 and CSC 2015
  Best spark ignited fuel economy at CSC 2014 and CSC 2015

## Slide 3: Miller Cycle 600 ACE Engine
Stock 12:1 compression ratio to preserve efficiency
Late intake valve closing for reduced pumping losses
Increased torque with turbocharger boost
Decreased BSFC from stock naturally aspirated
Improved vehicle performance—appeals to more riders

## Slide 4: Engine Modifications
 | Rotax 600 ACE | Kettering 600 ACE
Displacement | 600 cm3 | 
Configuration | Inline 180° Two Cylinder | 
Block Material | Aluminum | 
Valve Actuation | Dual Overhead Camshaft, Type 1 (Direct Acting Bucket) | 
Valves per Cylinder | Four | 
Compression Ratio | 12 | 
Bore x Stroke | 74 x 69.7 mm | 
Intake Valve Open/Close | 3 BTDC / 37 ABDC | 21 ATDC / 61 ABDC
Exhaust Valve Open/Close | 44 BBDC / 6 ATDC | 
Engine Control System | Bosch Motronic ME17.8.5 | Woodward MotoTron 128 Custom developed code
Electronic Throttle System | N/A | Custom torque-based
Ignition System | 35 mJ Coil on Plug | 96 mJ Coil near Plug
Engine Weight | 40 kg (88 lb) | 
Maximum Power | 42 kW (56 hp) | 54 kW (74 hp)
Maximum Torque | 55 Nm (42 ft*lb) | 69 Nm (51 ft*lb)
Fuel Compatibility | 91+ AKI Gasoline up to E-10 | 91+ AKI Gasoline up to E-85
Turbocharger | N/A | Garrett MGT1246 Hybrid
Maximum Boost Pressure | N/A | 1.6 bar absolute

## Slide 5: Late Intake Valve Closing
Simulation DOE shows most efficient:
  20 degree intake cam retard from OE
  Increasing intake charge pressure up to knock limit
Exhaust camshaft as intake cam: LC 126 ATDC, IVC 21 ABDC
Turbocharger provides intake charge pressure for high power

## Slide 6: Engine Management System
Full-Authority Engine Management
Electronic Throttle Control System
Enhanced cylinder balance

## Slide 7: Engine Mapping
Volumetric Efficiency
Lean Stability Limit
Spark Advance (Lean)

## Slide 8: High Energy Ignition Coils
Coils tested with 95 mJ secondary energy
2.25ms spark duration
High energy/long duration spark optimal for lean combustion
Trigger Signal
Secondary Current
Secondary Voltage
Primary Current

## Slide 9: Compressor Matching
Honeywell Garrett MGT1246Z hybrid turbocharger
  MGT1238Z Compressor, MGT1446Z Turbine
  Large turbine wheel and housing for low backpressure with large pulses from odd-firing engine

## Slide 10: Catalytic Silencer design
Silencer weighs 10 lb (6lb under stock)
Passive acoustic valve is in production on passenger cars
Resistive tuning attenuates low-frequency content
Valve opens with increased mass flow at high power levels
Catalyst integrated in silencer

## Slide 11: Emissions and Aftertreatment
Ideal
Three-Way Catalyst
Kettering Lean-Burn
Chart: Exhaust Temperature
| 4 | 3 | 2 | 1
Equalivance Ratio | 0.80729 | 0.75089 | 0.82155 | 0.85561
EGT Post Turbo | 480.7015 | 578.808 | 609.3306 | 746.8642
Chart: Uncatalyzed Emissions
| 4 | 3 | 2 | 1
Equalivance Ratio | 0.80729 | 0.75089 | 0.82155 | 0.85561
THC | 1156.101 | 1249.6283 | 745.571 | 338.9733
NOx | 418.0157 | 421.114 | 2756.6663 | 2591.7004
CO | 1463.6046 | 1111 | 897.0171 | 917.4533
Substrate | Ceramic
Density | 900 cells/in2
Size | 110mm x 116mm length
Loading | Platinum – 40 g/ft3
 | Rhodium – 8 g/ft3
 | Barium - Proprietary

## Slide 12: Dynamic Performance-Light Weight
499 lb with fluids, without fuel
Lightest snowmobile at CSC 2014 and CSC 2015
Best spark ignited fuel economy at CSC 2014 and CSC 2015
Cost-effective at $8657 MSRP

## Slide 13: Thanks to our Sponsors!