## Slide 1: Michigan Tech’s E-Rush
Presented by:
Terry Gregoricka
Adrienne Piron

## Slide 2: Abstract
2010 Polaris Rush
Electric Powered
Powered by Hi Performance Golf Cars AC-20
Curtis motor controller
CALB 70AH batteries
MTU designed rear drive system

## Slide 3: Design Strategy
Range
Towing capacity
Innovation
Safety
Weight, handling, acceleration, cost, and durability.

## Slide 4: Chassis and Electrical Design
2010 Polaris Rush
Lightweight
Adjustable rear suspension
Low cost
Rear mounted motor
Easily accessible
“All-in-one system”
HV and 12 V system

## Slide 5: DC to DC Converter
Mean Well SD-150D-12
Similar to AC Transformer
Complete Isolation between HV and LV
Isolation up to 1500V
Range of 72-144V

## Slide 6: Accumulator System
Batteries
Battery Management System

## Slide 7: Batteries
35 Lithium Iron Phosphate
Selected for stability characteristics
Chinese Aviation Lithium Batteries (CALB)
Connected in Series
Produces 114V (3.2V each)
Short time discharge rating of these cells is 700A

## Slide 8: Battery Management System
Was necessary to manage the batteries
Orion has one of the smartest BMS modules on the market
Thus can manage a large range of parameters
Monitors voltage, current, temperate, and controls the charging system

## Slide 9: Battery Containment
Goal was to maintain low center of gravity
Constructed using 1/8 inch 6061-T6 aluminum
Modeled to be similar to original engine
Analysis was done on CAD to apply loads

## Slide 10: Battery Containment

## Slide 11: Safety Precautions
Isolated display to prevent HV going to dash
Nomex and polycarbonate lined battery box
Bender IR155-3204 ground fault circuit

## Slide 12: Speed Control
Curtis 1238-7501 motor controller
Converts DC to AC
3 phase motor
Curtis Spyglass 840 for operator to view various parameters

## Slide 13: Motor and Motor Controller
Motor Controller under Charger
AC-20 Motor

## Slide 14: High Voltage Fusing
Only 1 fuse is in the battery pack
Rated for pack voltage and continuous ampere rating of the wire
Using a 250A Bussman slow blow fuse

## Slide 15: System Charging
On board charging system
1 kW delta-q, qui-q charger
BMS and charger are in communication
BMS states if it is safe to charge

## Slide 16: Power Transmission
Motor and brakes located in the rear
Leads to more efficient drive system
Direct motor to track system

## Slide 17: Weight
Stock chassis 271 lbs
Battery pack weight 192 lbs
Battery housing weight 25 lbs
Motor and controller 65 lbs
Final design weight 600 lbs

## Slide 18: MSRP
The total cost of our sled was calculated to be $16,041.47

## Slide 19: Thank You Sponsors!

## Slide 20: Thank You Sponsors!