## Slide 1: NDSU Clean Snowmobile
Presented by:
Michael Niehoff
Jared Quinlan
Advisor:
Dr. Robert Pieri

## Slide 2: Goals & Objectives
Complete Each Event
Retrofit a Diesel Engine into a Snowmobile
Achieve 25 mpg
Increase Soot Control
Refine Power Delivery to Track
Provide Optimal Utility Snowmobile

## Slide 3: Target Market
Utility Use
National Parks
Trail Riding
Commercial
  Longevity
  Low Maintenance

## Slide 4: Advantages vs. Disadvantages
Improved Fuel Economy
  Capable of long trips
  Reach remote locations
Improved Torque Output
  Pulling Capacity
  Workhorse
Long Track
  Improved traction for pulling
  Deep snow compatible
Cold Starting Issues
  Glow Plugs
“Dirty”
  Diesel Particulate Filter
  Diesel Oxidization Catalyst
Slow
  High-Low Gearing

## Slide 5: Chassis Selection
Utility Snowmobile
Indy Voyager
  Balance of Traction & Lower Weight
  Retrofit High-Low Transmission
  Modify Overstructure
 | IQ WideTrak | Indy Voyager
Track | Width: 20” Length: 156” | Width: 15” Length: 144” or 155”
Dry Weight (lbs) | 671 | 498
Gearing (jackshaft to driveshaft) | High-Low Transmission | Fixed Gear Ratio
Cargo Rack | Yes | Yes

## Slide 6: Engine Selection
3 Cylinder, 904 cc Yanmar Diesel
Lightweight
  187 lbs
Size Constraints
Passes 2008 EPA Tier 4
High Output Power
  23.4 Hp Stock
  50 ft-lb torque
Turbocharger
  IHI RHF3
  Increased Air Flow Rate
Photo Courtesy of Yanmar.com

## Slide 7: Emissions
Diesel Oxidation Catalyst
  Light-Off Temperature
    ~185°C-225°C
  Products
    Carbon Monoxide (CO)
    Hydrocarbons (HC)
    Particulate Matter (PM)
    Oxygen (O2)
  Reactants
    Carbon Dioxide (CO2)
    Water Vapor (H2O)

## Slide 8: Emissions
Diesel Particulate Filter
  Traps Particulate Matter
  Effective Filter Removes up to 85% of PM
  Regeneration Oxidizes Soot into Ash
    Regeneration ~650°C
  Peak EGT of ~450°C
    Requires Active Regeneration

## Slide 9: Noise Control
Track Noise
  Rubber skirting
  New bearings and bogey wheels
Exhaust Noise
  Direct into snow
  Insulation/Wrapping

## Slide 10: Outfitter Perspective
MSRP: $15,579.99
Diesel Engine
  Increased engine life over Gasoline
Diesel Fuel is readily available
High-Low Transmission
2” Receiver Hitch

## Slide 11: Conclusion
Utility Snowmobile
Efficient
Quiet
Clean

## Slide 12: Thank You to Our Sponsors
NDSU Mechanical Engineering Dept. & NDSU SAE Polaris Industries Team Industries Great River Energy Camoplast BASF Wheels Inc. Exhaust Pro's Al's Snowmobile Parts McNelius Steel Klim RJ Mann & Associates SolidWorks

## Slide 13: Questions?