## Slide 1: North Dakota State Clean Snowmobile Challenge 2015-2016
Presented by:
Steve Miller
Danika Gieske
Advisor:
Dr. Robert Pieri

## Slide 2: Outline
Introduction
Strategy and Goals
Design
  Engine
  Exhaust System
  Chassis Modifications
Conclusion
Questions

## Slide 3: Introduction
2016 SAE Clean Snowmobile Challenge
  Competing in the Diesel Utility Class
  Stricter Regulations are forcing snowmobile industry to change
    Tier 4 emission regulations have to be met
    By implementing a diesel engine into the snowmobile NDSU hopes to research and develop technology that isn’t commonly seen in the snowmobile industry.
  The target market for this sled are consumers looking for a long lasting and reliable snowmobile. This snowmobile is intended to be a working vehicle that can be used in a variety of applications.
    Towing large loads through snow
    Traveling long distances on a single tank of fuel
    Commercial projects
    Land owners, park managers

## Slide 4: Comparison
VS
“Big Frank”
4WD Utility Truck

## Slide 5: Goals and Strategy
Goals
  Design a snowmobile that is reliable and focused around the key values of the competition.
    Cleaner and quieter without sacrificing performance
Strategy
  Install a Diesel engine into Polaris Voyageur Chassis
  Incorporate a wall flow DPF
  Make necessary chassis modifications to incorporate diesel engine
  Market snowmobile to working class

## Slide 6: Why Diesel???
Roughly half of all passenger vehicles in Europe run off of Diesel fuel
From 2010-2015 the amount of diesel vehicles in the United States has doubled to 155,000
Larger energy content than gasoline
  139,000 BTU/Gal vs 124,000 BTU/Gal
  Translates into higher fuel economy
Cheaper long term cost
  Generally more expensive initially
(New York Times article)

## Slide 7: Engine Selection
3 Cylinder, 904cc Yanmar Diesel Engine
  23.4 hp stock
  50 ft-lb torque
  Mechanical fuel injection
  IHI RHF3 turbo charger
    Increased power to weight ratio
    Nearly doubles horsepower
  Passes 2008 EPA Tier 4
Photo from Yanmar.com

## Slide 8: Exhaust System
Volkswagen TDI Diesel Oxidation Catalyst (DOC) and Diesel Particulate Filter (DPF)
  DOC converts CO (Carbon Monoxide), HC (Hydro Carbons) and PM (Particulate Matter) to the compounds CO2 and H2O
  DPF primary objective is to remove soot from the exhaust
Switched from a partial flow DPF to a wall flow DPF
  Creates a much more efficient filtration system
  Partial flow filter has a valve that could let emissions exit without being treated
  Wall flow forces all emissions through the appropriate filtration
Active regeneration
  High temperatures burn soot instead of a fuel additive (passive regeneration)
Exhaust DPF and DOC

## Slide 9: Chassis Selection
2014 550 Polaris Indy Voyageur 144" fan cooled
  Longer track provides better traction in deep snow
  Long tunnel provides storage space for cargo
Large size of engine caused several major chassis changes
  Cooling system
  Steering
Other chassis modifications
  Towing hitch
  Battery box
  Hood sweep
Polaris Voyageur. Photo from Polaris.com
Hood sweep allows clearance for turbo

## Slide 10: Cooling System
  Indy Voyageur was originally fan-cooled
    To increase cooling, a liquid cooled system was installed underneath the tunnel
    Heat exchanger was taken from a liquid cooled Polaris Indy.
    Had to decrease width of heat exchanger to fit between tunnel
  Advantages
    Saves much needed space under the hood
    Allows the snow to maintain proper engine coolant temperature
CAD model of heat exchanger mounting

## Slide 11: Steering System
Stock steering wasn't able to be used due interference with turbo
  No direct path to steering outlet
  Steering was re-routed to the side of the engine
U-joint steering column
  Borgeson double u-joints
  3/4-inch DD steering shaft
  NTN mounted bearings
Components reused from the 2014 550 Indy Voyager steering system
  tie rod and mounting plate
U-joint steering linkage
Stock tie rod and mounting plate

## Slide 12: Snowmobile Features
Polaris floatation skis
  Provide a larger area for weight distribution
  Increase handling in deeper snow
Camso Cobra track
  Lug designs generate less noise
  Cupped lugs for superior acceleration & braking in loose, soft snow
  Flexible lug design for off-trail performance
Suspension
  Switched springs from stock 100lb/in to 155lb/in springs to ensure rider comfort and to prevent bottoming out due to heavy cargo
Camso Cobra track. Photo from Camso.com

## Slide 13: Design Challenges
Diesel engines are not common in the snowmobile industry
  Many components had to be custom fabricated
  Used parts from several industries: Auto, Agriculture and Snowmobile
Emissions from diesel engines are perceived as “Dirty”
  Black smoke coming out of the exhaust causes negative perceptions
  May leave black stains in the white snow
  Distinct exhaust order

## Slide 14: Conclusions
Diesel engines are work horses
  Long reliable engine life
Diesel fuel has a higher energy content than gasoline
  Increased fuel economy
  Allows for longer travel to remote locations
Increased towing capabilities
  Commercial application
  Able to haul large loads
Diesel emissions technology is advancing
  Cleaner and quieter exhaust systems
  Smaller size

## Slide 15: MSRP
Based on team estimates and the application of the sled, the MSRP for a mass produced version of this snowmobile would be $13,800
  Long life of engine and fuel economy make this an attractive offer to consumers

## Slide 16: Questions?