## Slide 1: Re-Engineering a 2015 Polaris Indy
2016 SAE Clean Snowmobile Competition
Presented by: Pryce McDaniel, Josh McCoy, Mike Waloch 3/7/16

## Slide 2: Outline
Snowmobile Choice
Chassis Improvements
  Big Wheel Kit
Noise Reduction
Fuel Economy and Emissions
  Conversion to Ethanol
  Real-Time Fuel Compensation
  Knock Control
  Exhaust Modifications
  Emission Results
Cost Effectiveness
Conclusion

## Slide 3: Snowmobile Choice
2015 Polaris Indy
  600cc Two-stroke
Why?
  Power to weight ratio
  Consumer appeal
  Large market demand

## Slide 4: Chassis Improvements Big Wheel Kit
Big wheel kit is designed to reduce the rolling resistance of the track.
Improves fuel economy.
Before
After

## Slide 5
-Skid and stock 7.5” rear wheel
Skid with relocation bracket
Bottom of wheel is tangent to skid
-Skid and stock 7.5” rear wheel
-Skid with 10” Wheel
Bottom of wheel not tangent to skid
Chassis Improvements Big Wheel Kit

## Slide 6: Chassis Improvements Big Wheel Kit
SolidWorks 2014
Yield Strength: 42,000 psi
Maximum Stress: 15,458 psi @ 500 lbf
Maximum Strain: 735 με
Minimum Factor of Safety: 2.74
Strain at 500 lbf
Stress at 500 lbf
Factor of Safety at 500 lbf
FEA Results

## Slide 7: Chassis Improvements Big Wheel Kit
Physical Experiment
Strain measurements taken with 3 element strain gauges
FEA and Lab experimental strain values matched within 20%
FOS was verified within
± 0.2
12% reduction in rolling resistance
Principal Strains Taken at Center of Bracket

## Slide 8: Noise Reduction
Additional mufflers
  Thrush glasspack
  Thrush Chambered turbo muffler
Results
  10% reduction in exhaust noise
  Structural integrity maintained

## Slide 9: Fuel Economy and Emissions Conversion to Ethanol
Vipec ECU
  Fuel tables
  Ignition tables
  Injection timing
  Knock Calibration
GM Flex Fuel Sensor
  Measure ethanol content
NGK AFX Air to Fuel Ratio gauge
  Tuning to 0.95 to 1.1 λ
Vipec Tuning Software

## Slide 10: Fuel Economy and Emissions Real-Time Ethanol Compensation
Fuel Compensation
Fuel increase for 0~100% ethanol
Linear scale based on % ethanol
Based on RPM and throttle position range

## Slide 11: Fuel Economy and Emissions Real-Time Ethanol Compensation
Ignition Compensation
Ignition timing advance by 0~4 ⁰BTDC
Based on RPM and throttle position range
Max 4 ⁰ advance

## Slide 12: Fuel Economy and Emissions Knock Control
Bosch KS-4-K1 Knock Sensor
Used for ignition trim
  Sampled between 10~40⁰ BTDC
  MAX delay of 4⁰ BTDC
Protects engine while running lean conditions

## Slide 13: Fuel Economy and Emissions Emissions Results: HC, NO, CO
Emissions data taken with a Horiba Mexa-584L
3.76% increase on average

## Slide 14: Fuel Economy and Emissions Emissions Results: HC, NO, CO
42.1% decrease on average

## Slide 15: Fuel Economy and Emissions Emissions Results: HC, NO, CO
44.9% decrease on average

## Slide 16: Cost Effectiveness
MSRP calculated for competition
  $13,518
Considerations
  Vipec: $2,195
  Axle Relocation bracket: $58
Adjusted MSRP
  $11,265

## Slide 17: Conclusion
Improved Emissions
  45% decrease in Carbon Monoxide
Full ethanol compensation
  Consumer could run E0 to E100
Exhaust noise reduced
10%
Cost effective

## Slide 18: Thank you to our sponsors!