## Slide 1: Re-Engineering a 2015 Polaris Indy
2017 SAE Clean Snowmobile Competition
Presented by: Josh McCoy, Mike Waloch, Nathan Zabel 3/7/16

## Slide 2: Outline
Snowmobile Choice
Chassis Improvements
  Big Wheel Kit
  Track Selection
Noise Reduction
Fuel Economy and Emissions
  Ethanol Correction
  Tuning
  Exhaust Modifications
  Emission Results
Cost Effectiveness
Conclusion

## Slide 3: Snowmobile Choice
2015 Polaris Indy
  600cc Two-stroke
Why?
  Power to weight ratio
  Consumer appeal
  Large market demand

## Slide 4: Chassis Improvements Big Wheel Kit
Big wheel kit is designed to reduce the rolling resistance of the track.
Improves fuel economy.
Before
After

## Slide 5
-Skid and stock 7.5” rear wheel
Skid with relocation bracket
Bottom of wheel is tangent to skid
-Skid and stock 7.5” rear wheel
-Skid with 10” Wheel
Bottom of wheel not tangent to skid
Chassis Improvements Big Wheel Kit

## Slide 6: Chassis Improvements Big Wheel Kit
SolidWorks 2014
Yield Strength: 42,000 psi
Maximum Stress: 15,458 psi @ 500 lbf
Maximum Strain: 735 με
Minimum Factor of Safety: 2.74
Strain at 500 lbf
Stress at 500 lbf
Factor of Safety at 500 lbf
FEA Results

## Slide 7: Chassis Improvements Big Wheel Kit
Physical Experiment
Strain measurements taken with 3 element strain gauges
FEA and Lab experimental strain values matched within 20%
FOS was verified within
± 0.2
12% reduction in rolling resistance
Principal Strains Taken at Center of Bracket

## Slide 8: Noise Reduction
Custom designed multi-chambered muffler
Design featuring chambers and perforated tubing
Forced to remove due to issues with backpressure

## Slide 9: Catalytic Converter
3 Way Catalyst designed through collaboration by BASF and Emitec
Mounted by modifying Sno-Stuff trail can
Heat shield and wrap used to protect other components from heat

## Slide 10: Fuel Economy and Emissions Conversion to Ethanol
GM Flex Fuel Sensor
  Measure ethanol content of fuel
Zietronix ECA
  Display ethanol content
  Convert frequency to 5 volt signal

## Slide 11: Fuel Economy and Emissions Tuning
Fuel Compensation
Auto tune to range of
Scale fuel using pressure correction table
Allows use to run near stoich at all ethanol contents

## Slide 12: Fuel Economy and Emissions Emissions Results: HC, NO, CO
Emissions data taken with a Horiba Mexa-584L
3922% decrease on average
Chart: HC (ppm)
| Mode 2 | Mode 4 | Mode 5
93 Octane | 3409 | 4736 | 9425
E75 | 4226 | 5625 | 9127
93 Octane w/ Cat | 84 | 108 | 256

## Slide 13: Fuel Economy and Emissions Emissions Results: HC, NO, CO
1268% decrease on average
Chart: NO (ppm)
| Mode 2 | Mode 4 | Mode 5
93 Octane | 311 | 220 | 154
E75 | 71 | 43 | 41
93 Octane w/ Cat | 34 | 12 | 8

## Slide 14: Fuel Economy and Emissions Emissions Results: HC, NO, CO
83% increase on average
Believe that calibration was not accurate
Chart: CO %
| Mode 2 | Mode 4 | Mode 5
93 Octane | 4.25 | 2.84 | 3.82
E75 | 3.42 | 1.57 | 3.36
93 Octane w/ Cat | 5.76 | 4.53 | 9.68

## Slide 15: Cost Effectiveness
Cost of stock snowmobile
  $8,399
MSRP calculated for competition
  $9,542.90
Key Factors for Increase
  Power Commander V
  Big Wheel Kit
  Custom exhaust system

## Slide 16: Conclusion
Improved Emissions
Full ethanol compensation
  Consumer could run E0 to E100
Cost effective

## Slide 17: Thank you to our sponsors!