## Slide 1: University of Wisconsin Platteville 2017 CSC Diesel Team
Presenters:
Brandon Miller
Matt Stedl

## Slide 2: Platform Choice
Chassis: 2017 Arctic Cat Bearcat 3000 LT
Engine Type | 4-Stroke
Engine Details | Liquid Cooled Kubota D902
Cylinders | 3
Displacement | 898 cc
Bore x Stroke (mm) | 72.0 mm X 73.6 mm
Exhaust | Single
Fueling | Indirect Injection

## Slide 3: Design Strategy
Clean
  Engine selection
  Diesel Oxidization Catalyst
Quiet
  Undercoating
  Sound dampening foam
Efficiency
  Driveline improvements
  Emissions targeting
Fuel Compatibility
  Bio Diesel 0-9%
User Friendly
  Ergonomic rider position
  Simple display and controls
  Motor reliability
  Adjustable suspension

## Slide 4: Consumer Appeal
Comfort
Reliability
  Engine life
  Mechanical fuel pumps
  Cold Start
Performance
  TrailTrac
  Towing capabilities
  GPS speedometer
Low Maintenance
  Belt drive
  Engine oil life
Low Operating Cost
  Fuel mileage

## Slide 5: Dealer Appeal
Manufactures
  Designed for ease of manufacturing
  Expandable market
Sales
  Marketable to consumers
    Aesthetics
    Performance
    Work horse styling
Service
  Readily available parts
  Ease of maintenance
  Simplicity

## Slide 6: Engine Selection
Kubota D902
  3600 rpm model
  Indirect Injection
  Average 24 hp
  Mechanical lifter pump and high pressure pump
  Overall dimensional size
  Dry weight of 159 lb

## Slide 7: Engine Tuning and Calibration
DYNOmite Water-Brake Dynamometer
Exhaust Gas Temperature
EMS Emissions Analyzer

## Slide 8: Exhaust System
Reducing Emissions
  Diesel Oxidation Catalyst
    Nett Technologies
Advantages
  Stock Bearcat 3000 LT
  Catalyst placement
  No maintenance

## Slide 9: Driveline Improvements
Belt Drive System
  C3 Powersports
Custom 10” Rear Idler Wheels
Graphite Infused Slides
Track
  Quiet Ramp Technology
Added Idler Wheels

## Slide 10: Sound Attenuation
Quiet-ramp track
Bogie wheels staggered and phased
Undercoating
Sound dampening foam
J1161

## Slide 11: Suspension
Easily Adjustable Suspension
Floating Front Rear Suspension
  Improved control
  Better traction

## Slide 12: MSRP Value
Estimated Value $12,094.13
$1,995.13 value over stock Bearcat 3000 LT

## Slide 13: Summary
Consumer Benefits
  Reliable
  Competitive Cost
    $12,094.13 USD MSRP
Dealer Benefits
Environmental Benefits
  Low Emissions
  Quiet
  Fuel Efficient

## Slide 14: Thank You!
Questions?