## Slide 1: University of Wisconsin-Platteville Clean Snowmobile
Internal Combustion

## Slide 2: Design Improvements
Improved steering system
  Lower Severity and probability of failure
Over structure redesign
  Snug to the engine
  Increase strength
Under seat fuel cell
  Lower center of gravity
Flex Fuel Capable
  Ethanol 0-85%
Engine controls
  Variable cam control
  Smart alternator control

## Slide 3: Chassis and Engine
Chassis: 2017 Arctic Cat ZR 7000 LXR
Engine Specifications:
Manufacture | Ford Motor Company
Stroke | 4 Stroke
Cooling | Liquid Cooling
Number of Cylinders | 3
Displacement | 999cc
Bore x Stroke (mm) | 71.9mm x 82.0
Fuel Delivery | High Pressure Direct Injection

## Slide 4: Over Structure
Custom X-Brace to support chassis and protect engine

## Slide 6: Engine Benefits
Ford 1.0 L EcoBoost
  Improved Reliability
  Direct Injection
International Engine of the Year:
  2012,2013,2014
1.0 L Engine of the Year
  2012,2013,2014,2015,2016,2017
World Wide Parts and Technical Support
Ethanol Content Fuels
Variable Cam Timing
100 ft-lbs of Torque from 1500 to 6000 rpm
Average of 100 hp

## Slide 7: Driveline Enhancements
Specialty Motorsport Belt Drive System
  12 Pounds in Weight Reduction
Rear 10’’ Diameter Billet Aluminum Wheels
Graphite Infused Slides
Idler Wheels Placement

## Slide 8: Ice Attack XT Track
Custom Camso Ported Track
Single ply for reduced weight
Quite Ramp Technology
In-lug Studs for Superior Traction and Braking Control
Chart: Scenario
| Stock 1 | Ported Track
 | 57.197 | 24.1212

## Slide 9: Noise Reduction
  Arctic Cat ZR 7000 Muffler for Reduced Noise Pollution
  Custom Airbox to limit intake noise
  Tunnel Undercoating

## Slide 10: Suspension
Easily Adjustable
Wide Stance for greater stability
Floating Front Rear Suspension
  Increased Traction
  Better cornering

## Slide 11: Controls and Displays
Hydraulic Steering for reduced rider fatigue
  Utilizes Mercury Helm and Cylinder
  4 to 1 Gear box ratio
Motec C125 Full Color
  Ability to monitor all engine systems

## Slide 12: Consumer Appeal
Rider Forward
Reliability
  Engine Life
  Diagnostics & Sensors
Performance
  Turbo Charged
  0-60 Time: 4.5 seconds
Low Maintenance
  Reduced Oil Changes
  Belt Drive
Lower Operating Cost
Part readily available
Fuel Mileage
  13 Miles Per Gallon on E85
  16 Miles Per Gallon on E15

## Slide 13: Dealer Appeal
Sales
  Marketable
    Performance
    Reliability
    MSRP: 18,811.67 USD
Service
  Parts Availability
  Easy to work on

## Slide 14: Acknowledgements and Questions
We would like to thank you all for taking time to listen to our presentation.
Any Questions?