## Slide 1: University of Wisconsin – Platteville 2019 SI Snowmobile Team
Presenters:
Camden Stoppleworth
Micheal Duenk

## Slide 2: Snowmobile Selection
Chassis:
  2017 Arctic Cat ZR 7000
Engine:
  Ford 1.0 L EcoBoost
Engine Type​ | 4-Stroke GTDI​
Engine Details​ | Liquid Cooled ​ Ford 1.0 L EcoBoost​
Cylinders​ | 3​
Displacement​ | 999cc​
Bore x Stroke (mm)​ | 71.9 mm X 82.0 mm​
Fueling​ | Direct Injection​

## Slide 3: Design Goals
Clean
  Modern engine
  Exhaust
Quiet
  Custom Camso track
Efficiency
  Engine management
  Driveline improvements
Flex Fuel
  Ethanol compatability of
  0-85%
User Friendly
  Simple display and controls
  Easy starting
  Low-maintenance

## Slide 4: Team Goals
Stock appearance
Lower engine operating RPM
Reduce emissions
Decrease intake and driveline noise
Driveablility

## Slide 5: Stock Appearance
2017 ZR 7000
  Yamaha Sidewinder panels
Engine orientation
Exhaust/intake routing

## Slide 6: Lower Operating RPM
Gear ratio change
  2.03:1 to 1.25:1
45 MPH cruising RPM
  4500 RPM from 2018
  3000 RPM currently

## Slide 7: Reduced Emissions
Engine Selection
  Ford 1.0L Ecoboost
    Variable Cam timing
    Direct Injection
    Turbocharged
Engine Management
  Motec M142 ECU
    Data logging
    Variable cam control
    Direct injection capable
Catalyst
  Ford 3-way catalytic converter
  Placement near turbocharger outlet

## Slide 8: Noise Mitigation
Rotax 900 ACE silencer
Camso quiet ramp track
Introvert drivers
Porous acoustic ducting

## Slide 9: Camso Track
Chart: Scenario
| Stock 1 | Ported Track
 | 57.197 | 24.1212

## Slide 10: Drivability
Engine calibrations
Clutch tuning
Gear ratio change
Mechanical steering
  Stock frog joint

## Slide 11: Driveline
Rear Wheels
  Replaced stock rear idler wheels with 10” diameter billet aluminum wheels
Graphite Infused Slides
Track
  Custom Camso Ice Attak XT
  Ported
  Quiet Ramp Technology
  In-lug Studs
  Single ply
Idler Wheels & Placement

## Slide 12: Consumer Appeal
Comfort
Reliability
  Engine life
  Diagnostics & sensors
High Performance
  Variable Cam timing
  Turbocharged
Low Maintenance
  No valve adjustment
  Timing belt
  Belt Drive
Low Operating Cost
  Fuel mileage

## Slide 13: Summary
Consumer Benefits​
Reliable​
Competitive Cost​
  MSRP of $18,412.70 USD
Environmental Benefits​
  Low Emissions​
  Quiet​
  Fuel Efficient​

## Slide 14: Thank You