## Slide 1: SAE Clean Snowmobile Challenge Design Presentation
2017 SAE Clean Snowmobile Challenge
Rochester Institute of Technology Clean Snowmobile Team
Eric Oswald & Dyllan Barnum

## Slide 2: Agenda
Introduction
Overview of Design Process
Define Stage
Measure Stage
Analysis Stage
Design Stage
  Chassis
  Bogie Wheels
  Engine Selection
Design Stage
  Engine Simulation
  Turbocharger Matching
  High Compression Pistons
  Intake Manifold
  Exhaust Muffler
  Liquid Cooled EGR system
  Flex Fuel
Conclusion
Questions

## Slide 3: Introduction
Presenters
Eric Oswald
  School Status: 4th year
  Major: Mechanical Engineering Technology
  Role: Project Manager/Powertrain Lead
Dyllan Barnum
  School Status: 5th year
  Major: Mechanical Engineering Technology
  Role: Chassis Design Lead
Team

## Slide 4: Overview of Design Process
Define: State problem, goals, and scope of project
Measure: Collect all relevant data to form a customer requirements list
Analyze: Use the customer requirements to create a cause and effect diagram
Design: Optimize designs using previous data to meet specifications
Verify: Show the design works within the design criteria and custom requirements.

## Slide 5: Define – Market Research
Purpose: To discover the main objective that the design needs to meet defined the scope of the project
Obtained: Usually through surveys from the rider, dealers, regulatory agency and the general public
VOC: Customer requirements can be represented by 6 major categories: Low Emissions, Noise, Fuel Efficiency, Performance, Reliability and Cost

## Slide 6: Measure – Pareto Chart
Used to create a visual on the heavy point break downs
Created targets to achieve and areas of focus
Highest scored categories
  Low Emissions
  Quiet Operation
  Fuel Efficiency
Chart: 
| Low Emissions | Noise | Fuel Efficiency | Performance | Reliability | MSRP
 | 350 | 300 | 300 | 200 | 100 | 50
 | 26.9231 | 50 | 73.0769 | 88.4615 | 96.1538 | 100

## Slide 7: Analyze – Benchmarking Competitors
Compared to the last year top 4 Clean Snowmobile Challenge teams
Added the 2016 RIT Clean Snowmobile Team to show improvement over the previous year
Used Pareto Chart to set goals based on importance of each category
Used other snowmobiles to set goals and show improvement areas
Numbers were calculated based on previous year’s results

## Slide 8: Analyze – House of Quality
HOQ helps to manipulate customer requirements into the product requirements that need to be met
Has the opportunity to adjust the product requirement
Shows the projected design compared to competitors
Data extracted is to meet customer requirements to optimize in Low Emissions, Quiet Operation and Fuel Efficiency

## Slide 9: Design - Chassis
Stock: 2016 Polaris Pro-S
Lighter weight/Increased handling from 2016 CSC Snowmobile
Rider forward position increases handling and control by centralizing mass
Utilization of stock mounting points for engine swap
Maintain stock clutch spacing

## Slide 10: Design – Rear Suspension
Stock bogie wheels are 6in in diameter made out of plastic
New set-up is 8in made out of 6061-T6 Aluminum
Using max engine torque there is a theoretical 7.66% reduction in friction
FEA was used in order to gain a perspective on how well our new design will hold up to the forces
Lowest FOS is 8, so there is potential for weight reduction

## Slide 11: Design – Engine Selection
Manufacturer: Weber
Displacement: 749cc
Usage: 2008 Polaris IQ Touring FST
Stroke: 4
Turbocharger: Stock
Compression Ratio: 9:1
Injection: Multi-Port Injection
Fuel Source: Gasoline
Stock Power: 140 HP

## Slide 12: Design – Engine Simulation
Use of 2 main simulation platforms
  GT Power
  ANSYS
Allows for quick design changes in order to see reaction in engine performance
Aided design in the following areas
  Intake Manifold
  Exhaust Muffler
  Turbocharger Matching
  Piston Selection
  Cam Shaft Selection

## Slide 13: Design – Turbocharger Matching
The MGT1238Z from Honeywell was selected
The use of a turbocharger is to increase the power of the engine without increasing displacement
GT Power simulation was used to confirm a correct match for both compression and turbine housing.
Upon simulation and testing the turbocharger was entering surge. In order to correct for this the internal wastegate was opened slightly to prevent surge.

## Slide 14: Design – High Compression Pistons
Stock turbo pistons were swapped for NA high compression pistons
Compression ratio went from 9.0:1 to 11.5:1
Concerns over engine knock were considered into the engine calibration
Improvements on engine torque and reduction in NOx were targeted

## Slide 15: Design – Intake Manifold
Due to the new chassis a new intake manifold design was necessary
New design also allowed for a closer placement of the ETC system. This will improve the response from the engine
Maintains the same flow rate as used in 2016 verified in Star CCM+ and GT-Power
Intake runner was optimized for torque using GT-Power

## Slide 16: Design – Exhaust Muffler
Designed to reduce noise of the overall snowmobile
Features various chambers to cancel targeted frequencies
Designed for EGR outlet accessibility
Back pressure and noise was minimized using GT-Power
Features integrated 3-way catalytic converter for ease of packaging

## Slide 17: Design – Liquid Cooled EGR
Uses inert exhaust gas to lower NOx within the combustion chamber
Exhaust gas is pulled through a cooler in order to reduce temperatures of the combustion to reduce knock tendency.
Increased temperature from the 2016 CSC system to reduce condensation

## Slide 18: Flex Fuel
Closed Loop O2 allowed for the engine to inject any type of fuel from E0 to E85 gasoline/ethanol mix
ECM reads lambda and adjusts fuel pulse width in order to maintain a fuel ratio
ECM has the ability to learn pervious engine operating parameters to adjust pulse width quicker
Injectors are sized correctly, according to GT-power to accept ethanol blended fuel

## Slide 19: Verify – High Compression Pistons
Torque
NOx Reduction

## Slide 20: Verify - Exhaust Gas Recirculation

## Slide 21: Verify – Engine Power

## Slide 22: Conclusion
RIT Clean Snowmobile Team was able to create a fuel efficient & lower emission snowmobile
Using various technologies such as, turbocharging, EGR, flex fuel, catalytic converter, custom intake/exhaust system, with a custom ECM controlling all systems.
Improvements can be made in the following areas for the RIT CST:
  Increased controllability of the EGR system
  Creating/comparing more test data
  Creating test data for stock snowmobile
  Time and project management skills

## Slide 23: Questions?