## Slide 1: SAE Clean Snowmobile Challenge Design Presentation
2019 SAE Clean Snowmobile Challenge
Rochester Institute of Technology Clean Snowmobile Team
Jeff Phelps and Lucas Miller

## Slide 2: Agenda
Introduction
Chassis
Engine
Team organization
Overview of Design Process
Project Planning
Solutions
  Muffler Redesign
  Throttle body sizing
  Calibration strategy
  Flex Fuel
Conclusion
Questions

## Slide 3: Introduction
Presenters
Jeff Phelps
  School Status: 4th year
  Major: Mechanical Engineering Technology
  Role: Project Manager
Lucas Miller
  School Status: 5th year
  Major: Mechanical Engineering Technology
  Role: Engine Tuning & Calibration
Team

## Slide 4: Chassis
2016 Polaris Rush pro-s
Curve Industries xs skis
Increased front spring rate

## Slide 5: Engine
Manufacturer: Weber
Displacement: 749cc
Usage: Polaris FS IQ Touring
Stroke: 4
Compression Ratio: 11.5:1
Injection: Multi-Port Injection
Fuel Source: Gasoline
Stock Power: 80 HP
http://www.weberpower.com/mpe.html

## Slide 6: Team Structure

## Slide 7: Overview of Design Process
  Using the 2018 CSC as a baseline for the 2019 design season, the team utilized the experience to identify key issues and low scoring categories.
  The DMAIC process has been used for multiple years as it allows a clearly defined workflow throughout the year for each of the groups within the team.

## Slide 8: Project Planning
2018 Benchmark
Muffler Issues
  High noise levels
  Bolt in catalyst loosening
Oil leak issues
  AN fittings vibrating loose
Engine mounting issues
  Improper clutch spacing
Inability to Cold Start
Idle issues

## Slide 9: Solutions
Approaches selected
Muffler Issues- Full Redesign
Oil leak issues- switch back to hose clamps
Engine mounting issues-Engine Mount Redesign
Inability to Cold Start- logging starts
Idle issues- Reduce throttle body size

## Slide 10: Muffler Design- Components
Inner Cone with cut out slots
Outer Cone to guide the reverse flow
Catalytic Converter
Perforated Tube wrapped with glass fiber sound
absorbent packing material
Inlet and Outlet pipes

## Slide 11: Muffler Design-Flow
Inlet Flow through Catalytic Converter to Inner Cone with Slots
Flow exits slots from inner cone and is guided back by the outer cone
Flow escapes outer cone through a gap between the face of the outer cone feature and the top inner wall of the shell
Flow circulates in the top chamber and exits through the perforated tube

## Slide 12: Muffler Design- Sound Wave Flow Principles
Cones act as a baffling device by reducing the volume of the entering sound waves
Sound waves reflect off the cone, interfering with the entering sound waves, cancelling each other out
Reducing the size of the slots in the cone benefits the sound dampening
Reducing the gap distance between the outer cone feature and the top inner shell wall limits the amount of flow that can escape, reducing the noise
Perforated tubes dissipate the sound wave energy by converting them to heat energy through frictional dampening via the perforated holes
Sound absorbent packing material reduces the high pitch sound waves

## Slide 13: Throttle Body Size Reduction
Idle was too high during 2018 comp
No vacuum leaks were identified
Throttle position at idle was at minimum
Switch to a smaller throttle body (54mm to 46mm)
This allowed for lower clutch engagement speed
No decrease in peak power was seen

## Slide 14: Engine Calibration Strategy
Stoichiometric for cruising loads and speeds
Increased fueling outside of typical cruising range
  Increased power
  Decreased Nox
  Decreased Cylinder Temperatures and Increased Reliability
Data Logging
  Used to refine initial fuel table from dyno
Knock Sensor used for spark and fuel correction for Ethanol

## Slide 15: Flex Fuel
Closed Loop O2 is utilized to allow the engine to run any type of fuel from E0 to E85 gasoline/ethanol mix
ECM reads lambda and adjusts fuel pulse width in order to maintain stochiometric conditions
ECM has the ability to learn pervious engine operating parameters to adjust pulse width quicker
Accidental testing shows that the engine is not capable of switching to a gas/ethanol/diesel mixture using this approach

## Slide 16: Conclusion
A reduction in noise and emissions was attained
Rider comfort and appearance were maintained
Technologies utilized
  Engine swapped
  3d printed Intake
  Custom designed and fabricated exhaust system
  Engine tuning & dynamometer time

## Slide 17: Questions?