## Slide 1: SDSMT Zero Emissions Snowmobile
Bennett Prosser, Kyle Roe

## Slide 2: Overview
Goals
System Overview
Operator Perspective
Dealer/Outfitter Perspective
Environmental Impacts
Test Results

## Slide 3: Who We Are
SDSMT Student Organization with focus on ZE sled
Undergraduate ME and EE students
  4 Juniors
  3 Sophomores

## Slide 4: Goals
Develop electric snowmobile based on existing IC chassis
Approach performance levels of current gasoline sleds
  Acceleration
  Handling/Capability
  Range
  FUN

## Slide 5: System Overview
2014 Polaris Switchback Assault
Brammo 15/90 Li-ion battery modules (6)
  88.8V, 90Ah, 7.98kWh
Sevcon Gen4 motor controller
Parker/Brammo GVM1425 liquid cooled PMAC motor
  56hp peak, 67lb*ft
Safety systems
  Brammo BMS
  Bender IMD
SDSMT ZE Snowmobile – 2014 Switchback

## Slide 6: Operator Perspective
Functions like conventional snowmobile
Crossover chassis - benefits
Range
  Wh / [V * I / mph] = D
  D = 36 miles at 20mph
Peak torque and power at
  low motor rpm
Ergonomics and comfort
Seat concept

## Slide 7: Dealer / Outfitter Perspective
Modular design allows for easy maintenance
  Removable battery container
  Fault indication lights – BMS, IMD
  Fault reporting and logging from controller
  Diagnostic software for BMS, batteries, controller
Fault lights and data display

## Slide 8: Dealer / Outfitter Perspective
Components reduce maintenance needs
  Gates Polychain direct drive belt
    No cleaning, no clutch tuning
  Only annual maintenance changing chain-case oil, checking coolant levels
Direct-drive belt and motor
Aluminum Battery container

## Slide 9: Dealer / Outfitter Perspective
Cost
  Initial cost is high high end components and performance
    Quality, value
  Minimal operation costs mitigate higher initial cost
Top view without plastics

## Slide 10: Environmental Perspective
Zero source emissions
Energy consumption significantly less than IC snowmobile
Sealed motor compartment
Light weight = softer treading
Minimal noise impact
  Only noise from belt and track drive
Light weight being demonstrated

## Slide 11: Results / Testing
2012/2013 concept capable of 20 miles with 8kWh battery
  2014 concept loses 200+ lbs
    With same 8kWh capacity
  30+ mile range
  Healthier batteries
Strong acceleration
Good handling
Cold weather capability
Brammo 15/90 Li-ion module
Photo: Brammo Inc.

## Slide 12: Summary
Goals
System Overview
Operator Perspective
Dealer/Outfitter Perspective
Environmental Impacts
Test Results

## Slide 13: Questions?