## Slide 1: St. Cloud State University Slick Cylinders
SAE Clean Snowmobile Team

## Slide 2: Presentation Overview
About the Team
Design Process
Major Modifications
Catalytic Converter Selection
Tuning
Side by Side Comparison
Sponsors
Questions

## Slide 3: Team Members
From Left: Dan Kezar, Jake Harper, Heather VanSlyke, Jim Wicklund, Travis Meyer, & Gene Studniski

## Slide 4: Design Process
Sled Selection
2015 Polaris Rush 800 Pro-S
  MSRP: $12,799
  Stock Sled Weight: 431 lbs (Dry)
  Stock Engine: 154 hp 2-stroke
  Track Length: 120”
Engine selection
  2016 Polaris RZR XP 1000
  110 hp 4-stroke DOHC Twin Cylinder
  Max torque of 72 ft-lbs
  Wet Sump Oil System & Liquid Cooling

## Slide 5: Design Process
  Artec 3D scan of chassis and engine
  Design parts based off of the scan
Notes: Most of the innovation and modifications to the sled came from the necessity of fitting the larger 4 stroke engine in the the chassis of the rush pro s

## Slide 6: Major Modifications
  Engine Mount
  Support plate
  Steering Column
  Battery and Radiator Mount
  Air box
Notes: Unfortunately we did not manage to dyno because it broke down the day we were scheduled to test.

## Slide 7: Catalytic Converter Selection
  Benefits of Catalytic Converter Selection:
  Very Similar Specifications between 2008 Chevrolet Aveo and 2015 RZR Engine
    1600cc vs 999cc
    103hp vs 110hp
    2.5” pipe diameters
  Distance to engine block comparable
    3ft on Aveo vs. 1ft on this sled
  Temperature range
    Reaction range of 500F - 800F
    Measured 765F
Notes: This catalytic converter features a ribbed body that minimizes expansion and distortion when the converter heats up. These ribs form a channel that protects the cushioning mat from direct exposure to exhaust gases, and they hold the ceramic catalyst in proper alignment. The converters use a monolithic honeycomb catalyst which is designed for maximum flow and surface area. The manufacturer of the catalytic converter states that it will begin reacting at 500°F. For the new RZR 1000 engine the temperature at peak RPM will be 763°F leaving an adequate range of temperature for the converter to fully operate.

## Slide 8: Tuning

## Slide 9: Side by Side Comparison
Stock Rush 800 Pro-S
  2 stroke
  546 lbs wet
  154 hp
  102 ft-lbs of torque
  $12,799
Modified Rush XP 1000
  4 stroke
  620 lbs wet
  110 hp
  72 ft-lbs of torque
  Catalytic converter
  $13,801

## Slide 10: Thank You to Our Sponsors
VanSlyke Family
Josh Muonio
Jeff Hegle
Meyer Family

## Slide 11: Questions?