## Slide 1: University of Minnesota-Twin Cities
SAE International Clean Snowmobile Challenge 2017

## Slide 2: 2015 Polaris Indy 600 SP
600cc 2 stroke Liberty engine
Rated 125 hp
Fox IFP shocks

## Slide 3: Modification Overview
Skis and Track
Exhaust and Catalyst
Sound Deadening Foam
Standalone ECU and Ethanol Sensor

## Slide 4: Handling
C&A Pro TRX Skis
Camso Ice-Attack XT Track

## Slide 5: Exhaust System
Incorporates catalyst and a new muffler
Baffled to reduce noise
3-Way Catalyst
BASF TEX-0587 coating
Catalyst density 300 cells per square inch
2/9/1 ratio (Pt:Pd:Rh)

## Slide 6: Noise Reduction
Impedance tube and software
Allows testing of materials
Measures absorption coefficient
Best material tested was incorporated on sled

## Slide 8: Engine Management
Performance Electronics PE3
Standalone ECU
Supports 0-100% Ethanol mixtures
Air/Fuel ratio calibration strategy

## Slide 9: Sled Overview
0-100% Ethanol Capable
Handling upgrades for on-trail performance
Quieter exhaust muffler and aftertreatment
Sound deadening materials

## Slide 10: Acknowledgments
Our Sponsors: Polaris, BASF, Heraeus, Camso, C&A Pro, Ford, Celestica, Race Coatings, Minnesota Measurements, Toro, and others
Michigan Tech and the Keweenaw Research Center
SAE International
Judges and Volunteers

## Slide 11
Chart: Frequency (Hz)
| 40 | 50 | 63 | 80 | 100 | 125 | 160 | 200 | 250 | 315 | 400 | 500 | 630 | 800 | 1000 | 1250 | 1600 | 2000 | 2500
NoSample-1-1 | 0.016483 | -0.031226 | -0.010989 | -0.0027529 | -0.0724 | -0.067141 | 0.023121 | -0.038564 | 0.097244 | 0 | 0.029135 | -0.034924 | -0.00036553 | 0.0098846 | -0.032975 | -0.047052 | 0.057886 | 0.015013 | 0.52529
NoSample-1-2 | -0.029153 | 0.025549 | 0.03274 | -0.027776 | -0.032965 | -0.010568 | -0.036142 | 0.044761 | 0.09209 | 0.020725 | 0.050947 | -0.030907 | -0.007322 | -0.0055111 | -0.26908 | 0.41596 | -0.0415 | -0.11059 | -1.6592
NoSample-1-3 | -0.0609 | 0.051939 | 0.022099 | 0.027396 | 0 | -0.029351 | -0.0059435 | -0.0026368 | 0.084487 | -0.011922 | -0.053206 | 0.030807 | 0.0025517 | -0.0099888 | -0.19307 | -0.47674 | -0.0051282 | -0.010735 | 0.53894
NoSample-1-4 | -0.034629 | 0.030322 | -0.0084925 | -0.041866 | 0.026524 | -0.051308 | -0.0029873 | 0.013132 | 0.010568 | 0.032138 | 0.1261 | -0.13673 | -0.002925 | -0.0022161 | 0.067207 | -0.98981 | -0.092729 | -0.013216 | -2.6374
NoSample-1-5 | -0.0084925 | -0.016759 | -0.022566 | -0.039377 | 0.0079523 | -0.007767 | 0.0058565 | 0 | -0.086593 | -0.048114 | -0.0085653 | -0.031061 | -0.0010924 | 0.0087503 | -0.035439 | -0.13045 | -0.0076579 | 0.0083073 | -0.61881
Average | -0.023338 | 0.011965 | 0.0025582 | -0.016875 | -0.014178 | -0.033227 | -0.0032191 | 0.0033383 | 0.039559 | -0.0014346 | 0.028882 | -0.040562 | -0.0018306 | 0.00018377 | -0.092671 | -0.24562 | -0.017826 | -0.022244 | -0.77024