## Slide 2: Overview
Project Management
Base Sled Selection
Engine Management
Muffler Design and Catalyst Implementation
Noise Reduction

## Slide 3: Project Management
Focus on project selection
Projects that can be done with resources we have
Identify risks and create mitigation plans

## Slide 4: Base Sled Selection
2015 Indy 600 SP | 2016 Switchback 600
121 inch track | 137 inch track
449 lbs | 447 lbs
$9599 MSRP | $11,899 MSRP
Pro-Ride Chassis | Axys Chassis

## Slide 5: Engine Management
Dynojet Power Commander V
Low-risk
Ease of returning to stock
Dyno tuning not needed for a running sled
Has the features we needed
Ethanol Sensor

## Slide 6: Catalyst Selection
Heraeus 1:20:1 Three-way catalyst
Chart: Mode 5 HC Emissions
| Mode 5 HC Emissions (%)
No Catalyst | 1.13
Heraeus 1:20:1 | 0.02
HC conversion prioritized
Upsized from 70x75mm to 72x130mm
98.23% Mode 5 HC Conversion efficiency

## Slide 7: Muffler Design
Three-chamber muffler
Catalyst housed in muffler entrance
“Box” used as catalyst heat shielding

## Slide 8: Muffler Simulation and Results
Peak backpressure of 0.692 PSI
Destructive interference

## Slide 9: Target Frequency Identification
Competition sound files of 2017 CSC analyzed
Top 4 teams considered
200-2000 Hz loudest for all teams
Chart: Frequency Comparison (dBA Weighted)

## Slide 10: Exhaust Pressure Measurement
Measurement of exhaust pressure before and after the expansion chamber shows a change in pressure wave frequency.
7500 RPM
Across all RPM

## Slide 11: Impedance Tube
Added a second microphone to quantify sound reflection
Various improvements to test setup improved accuracy
  Square Wave Sine Wave
  Op-amps on microphones

## Slide 12: Sound Materials
Coatings were tested on ABS samples similar in thickness to the side panels
Flex Seal and Caulk were found to reduce a resonance in the system at 1000Hz, a target frequency
Flex Seal was applied to the interior of side panels

## Slide 13: Summary
Fun sled with over 100HP and 137” track
Flex fuel capability
Significantly reduced emissions
Sound deadening aimed at reducing unpleasant resonances
MSRP value of $12,083.52

## Slide 14: Thanks to Sponsors and Organizers

## Slide 15: Questions?

## Slide 16
Resonator

## Slide 17
Resonator

## Slide 20: Transmission Loss Calculation

## Slide 21
Appendix A-1: Speaker output when square wave excitation is applied

## Slide 22
Appendix A-2: Speaker output when sinusoidal excitation is applied

## Slide 24
 | Idle | 3000RPM | 4000RPM
Temperature | 698C | 852C | 856C
O2 | 5.4% | 1.5% | 0.8%
HC | 0.02% | 0.09% | 0.06%
CO2 | 11% | 15.4% | 10.7%
CO | 154ppm | 754ppm | 6852ppm
NO | 65ppm | 271ppm | 21ppm
Before Catalyst | 
HC | 1.13%
CO2 | 2.0%
CO | 3.05%
NO | 40ppm
NO2 | 2ppm
NOx | 43ppm