## Slide 1: University of Waterloo 2014 Clean Snowmobile

## Slide 2: Strategy
Four-stroke engine
  Weber MPE 750 Turbo (2 cyl)
Lightweight cross-country chassis
  Better control = less need to decelerate and accelerate
  2012 Polaris Rush
Inexpensive Weight Reductions
  Lithium Iron Phosphate Battery
  Aluminum Muffler
Improved traction and reduced drivetrain losses
  Prestudded track (Camoplast ICE Attak XT)
  Large diameter rear idler wheels
Part of a long term plan
  Stay tuned for next year

## Slide 3: Engine Selection
Weber MPE 750 Turbo
  2 cylinder
  750 cc
  Four stroke
  Turbo charged
snowmobile.com

## Slide 4: Chassis Selection
2012 Polaris Rush
  Easy to service
  Good handling
  Fairly lightweight
  Added bonus: free
    (Thanks Polaris!)
Polaris
Click to add text
Click to add text
Click to add text

## Slide 5: Modifications

## Slide 6: Lithium Iron Phosphate Battery
Antigravity
12 cell
small volume
Weight < 2 lbs
360 cold cranking amps
Antigravity Batteries

## Slide 7: 3 Way Caesium Catalytic Converter
Operator perspective: clear conscience
Dealer/rental: environmental appeal as a selling point
Environmental: targets CO, HC and NOx

## Slide 8: Muffler
Single element re-entrant diffuser
Aluminum construction
Weight < 5 lbs
Targets 6500 rpm
  (on a 3-cyl)

## Slide 9: Track
Camoplast Ice Attak XT
Pre-studded
1.22" lug profile
Traction and stability allows rider to maintain speed - less fuel burned from excessive need to accelerate and decelerate
Added traction can contribute to safety

## Slide 10: 8" rear wheels
Larger rear wheels
Offset axle
Less dynamic track deformation
Lower bearing speed

## Slide 11: Next steps
Reduce track noise
Means of reducing pumping losses (stay tuned!)
  EGR?
  More exotic means...
Refine fuel map and load calculation strategy
  Consistency of load state calculation
Weight reduction
New muffler design
  integrated catalyst

## Slide 12: Thank you! Questions?
sled.uwaterloo.ca
uwsled@gmail.com