## Slide 1: 2015 University of Waterloo Clean Snowmobile

## Slide 2: Philosophy
Develop a platform that meets competition objectives while providing a significant design challenge and engaging student and public interest by being unconventional and exciting.
Provide an open and friendly environment in which students can gain experience and develop skills that will enrich their undergraduate experience and benefit them professionally.

## Slide 3: Base Snowmobile
2013 Polaris Rush 600
Upgraded to align with 2014 Pro-R Model
  Competition MSRP requires current model
Donated by Polaris Industries

## Slide 4: Engine Selection
Weber MPE 750 Turbo
Originally used in Polaris FST models
750cc, 2 cylinder, four-stroke
143hp @ 7750rpm
  Over 130hp limit
  Less disincentive to de-tune

## Slide 5: Design Process
Six criteria chosen to weigh against CSC scoring
Weighting represents impact based on prior experience
Used to evaluate relative merit of various design alternatives
Efficiency | 20%
Emissions | 21%
Weight | 16%
Power | 8%
Noise | 18%
Reliability | 17%

## Slide 6: 2015 Design
Miller Cycle conversion
Electronic throttle control
Stoichiometric calibration with three-way catalytic converter
2.86” pitch track
Large diameter rear idler wheels
Balanced approach of engine, control, and driveline efficiency
Systems with modularity and little inter-dependence
  Contingency if a system was delayed/failed

## Slide 7: Miller Cycle
Trade displacement (power) for efficiency
  Power drops by ~15%, efficiency gain of ~3%
Expansion ratio is greater than compression ratio
  More work per unit of air-fuel charge
  Efficiency gain when maintaining trapped compression ratio
  Achieved with higher compression piston and custom camshaft with late intake valve closing
Good way of increasing efficiency of a turbocharged engine without knocking

## Slide 8: Miller Cycle
11:1 Piston
  Forged aluminum
  Lateral gas ports for top ring
  Large accumulator groove between rings
  Increased wrist pin lubrication
Custom Camshaft
  Added 15° intake valve duration, retarded by 13.5°
  Tradeoff between available grinds, approaching desired intake valve closure, and maintaining valve overlap
Chart: Crank Angle (°)
Ideal Modified Valve Closure | 267.0594
Stock Valve Closure | 323.5878

## Slide 9: Miller Cycle
Snowmobiler Perspective
  Better fuel economy
  Engine still just as durable
Outfitter/Dealer Perspective
  Modification is largely invisible to user
  Engine durability
Environmental/Landowner Perspective
  More complete burn (specific emissions)
  More efficient (overall emissions)
  Quieter (less effective displacement)
Chart: Crank Angle (°)
Ideal Modified Valve Closure | 267.0594
Stock Valve Closure | 323.5878

## Slide 10: Electronic Throttle Control
Electronic Throttle Control ‘decouples’ user power demand from powertrain response
  Reduce throttling losses
  Can ‘damp’ transient response
Allows drastically different powertrain response without changing engine calibration
  Same steady-state performance
Throttling losses in SI are significant at part load
Throttle opening is usually tied to power demand from rider
  Good for normally aspirated systems
  Turbocharged engines have other means of power modulation (wastegate or variable nozzle)
  Counter-intuitive that turbocharger is ‘fighting’ throttle at part-load
Mechanical throttle control also transfers harsh transients from rider over bumps, etc

## Slide 11: Electronic Throttle Control
Motec M400 ECU
  Processes analog values from request unit
  Translation table, with throttle safety switch
Motec DBW4
  Independent feedback control of throttle bodies
  Emphasis on safety
CAN Network
  Decentralized control
  Allows dedicated data-logger
CAN
Cable

## Slide 12: Electronic Throttle Control

## Slide 13: Electronic Throttle Control
Dealer/Outfitter/Manufacturer Perspective
  System is modular (upgrade path, assembly line)
  System is invisible to the user
  System can be marketed as high-tech
  Opportunity for different response based on rider experience
Environmental perspective
  A ‘BAT’ package can use a smoother throttle response to reduce emissions from harsh transients
Snowmobiler Perspective
  Improved fuel economy
  Extraordinarily responsive if so desired
  Extraordinarily forgiving if so desired
  Expensive components are protected inside the snowmobile
  Familiar throttle cable feel

## Slide 14: Emissions After-Treatment
Three-Way Catalytic Converter
  Effective way of dramatically reducing tailpipe emissions
  Widely available technology
Integrated into muffler
  Muffler fits inside sled – no more mogul-buster!
Completed assembly is ~11lb
No impedance of snowmobile manoeuverability
Next iteration will deal with increased backpressure
Chart: Airflow (CFM)
| 27.9 | 37.200000000000003 | 46.7 | 58 | 66.3 | 75 | 85.7 | 96.3 | 102.2 | 115.1 | 124.6 | 130.69999999999999 | 139.19999999999999 | 149.69999999999999
Stock Rev Muffler | 0.385 | 0.582 | 0.832 | 1.188 | 1.513 | 1.9 | 2.45 | 3.02 | 3.37 | 3.83 | 4.45 | 4.91 | 5.56 | 6.3
Custom Muffler With Spring | 1.29 | 2.26 | 3.12 | 4.059 | 4.734 | 5.343
Custom Muffler No Spring | 0.398 | 0.625 | 0.973 | 1.463 | 1.893 | 2.463 | 3.023 | 3.584 | 4.223 | 4.864

## Slide 15: Drivetrain
Large diameter rear idler wheels
  Reduce bearing and track losses at rear axle
  Inelastic behaviour of track under bending strain
  Proportional to strain, therefore proportional to curvature (inverse of wheel radius)
Rear idler wheels are the point of greatest curvature (7.125” diameter)
8” wheel reduces losses by around 10%

## Slide 16: Drivetrain
2.86” Pitch Track
  Camoplast ICE Attak XT, 120”
  1.2” lug, pre-studded, 37lb
  3lb savings over 2.52” pitch version (121”)
Use of pre-studded track allows for increased traction and control
  Only 2lb heavier than the stock track for 2013 600 Pro-R

## Slide 17: Challenges Encountered
Limited dynamometer availability
  University requires their (part-time) operator present
  Many teams vying for dyno time
  Very little dynamometer tuning was performed
  Cut short by alternator pulley excitement
Fabrication delays
  Decreased occupancy limit in student machine shop with highest demand ever
  Understaffing of engineering machine shop
  Several critical components weren’t completed until last week

## Slide 18: Summary
Snowmobiler Perspective
  Four-stroke reliability and longevity
  Capable of high performance
  Premium suspension
  Familiar look and feel
Dealer/Outfitter/Manufacturer Perspective
  Modularity and configurability
  Reliability/longevity
Environmental Perspective
  Reduced fuel consumption
  Reduced emissions

## Slide 19: Questions?