## Slide 1: 2016 University of Waterloo Clean Snowmobile

## Slide 2: Philosophy
Embrace design challenges
Engage students and public through originality
Open and safe learning environment for students
3 Year Cycle
Focus on reliability

## Slide 3: Design Criteria
Six criteria chosen to weigh against CSC scoring
Weighting represents impact based on prior experience
Used to evaluate relative merit of various design alternatives
Efficiency | 20%
Emissions | 21%
Weight | 16%
Power | 8%
Noise | 18%
Reliability | 17%

## Slide 4: Before this year
2013 Polaris Rush 600
Upgraded to align with 2014 Pro-R Model
  Competition MSRP requires current model

## Slide 5: Engine Selection
Weber MPE 750 Turbo
Originally used in Polaris FST models
750cc, 2 cylinder, four-stroke
143hp @ 7750rpm

## Slide 6: 2016 Design
Overall
  Balanced approach of engine, control, and driveline efficiency
  Systems with modularity and independence
Engine
  Miller Cycle
  Electronic throttle control
  Stoichiometric calibration
Drivetrain
  E-CVT
  Increased track pitch
  Increased idler diameter
Exhaust System
  3 way catalytic converter
  Replaceable configuration

## Slide 7: Miller Cycle
Trade displacement (power) for efficiency (3% efficiency gain, 15% power loss)
Expansion ratio is greater than compression ratio
11:1 pistons 30 degree later valve closing produces stock 9:1

## Slide 8: Electronic Throttle Control
Motec M400 ECU
  Processes analog values from request unit
  Translation table, with throttle safety switch
Motec DBW4
  Independent feedback control of throttle bodies
  Emphasis on safety
CAN
Cable

## Slide 9: Electronic Throttle Control

## Slide 10: Electronic Throttle Control
Dealer/Outfitter/Manufacturer Perspective
  System is modular (upgrade path, assembly line)
  System is invisible to the user
  System can be marketed as high-tech
  Opportunity for different response based on rider experience
Environmental perspective
  A ‘BAT’ package can use a smoother throttle response to reduce emissions from harsh transients
Snowmobiler Perspective
  Improved fuel economy
  Extraordinarily responsive if so desired
  Extraordinarily forgiving if so desired
  Expensive components are protected inside the snowmobile
  Familiar throttle cable feel

## Slide 11: Drivetrain
Large diameter rear idler wheels
  Reduces bearing and track losses

## Slide 12: Drivetrain
2.86” Pitch Track
  Camoplast ICE Attak XT, 120”
  1.2” lug, pre-studded, 37lb
  3lb savings over 2.52” pitch version (121”)
Use of pre-studded track allows for increased traction and control
  Only 2lb heavier than the stock track for 2013 600 Pro-R

## Slide 13: New for 2016
Exhaust System
E-CVT

## Slide 14: Testing, yes testing.
BSFC Map

## Slide 15: Testing, yes testing.
Clutch position

## Slide 16: Testing, yes testing.
Clutch Efficiency

## Slide 17: Electronic Continuously Variable Transmission

## Slide 18: Electronic Continuously Variable Transmission

## Slide 19: Electronic Continuously Variable Transmission

## Slide 20: Emissions After-Treatment
Three-Way Catalytic Converter
  Dramatically reduces emissions
  Widely available technology
Muffler and Resonator
  Targets a wide range of sound frequencies
Complete assembly is 15lb
Reduced Backpressure
  High flow muffler and resonator
  2” tubes

## Slide 21: Emissions After-Treatment
Three-Way Catalytic Converter
  Dramatically reduces emissions
  Widely available technology
Muffler and Resonator
  Targets a wide range of sound frequencies
Complete assembly is 15lb
Reduced Backpressure
  High flow muffler and resonator
  2” tubes

## Slide 22: Emissions After-Treatment
Stock Wideband lambda
  PID tuned for environment instabilities
  Changes PID parameters based on rpm
  Modifies open loop fuel table by up to +/- 20%
  Can maintain lambda within +/-0.02 with constant input

## Slide 23: Summary
Snowmobiler Perspective
  Four-stroke reliability and longevity
  Capable of high performance
  Premium suspension
  Familiar look and feel
Dealer/Outfitter/Manufacturer Perspective
  Modularity and configurability
  Reliability/longevity
Environmental Perspective
  Reduced fuel consumption
  Reduced emissions

## Slide 24: Questions?